## Slide 1: Unsimplified Datapath with Forwarding
Yes:
add
sub
and
or
slt
sw
No:
lw
beq
j
This design has:
logic for synchronizing control signals and instructions
forwarding logic
no hazard detection.

## Slide 2: Load-Use Data Hazard
Consider the following sequence of instructions:
lw $t2, 20($t1) # writes a value
and $t4, $t2, $t5 # reads that value
This hazard cannot be resolved by simple forwarding… why not?
and lw
The value lw writes into $t2 is not available until lw completes the MEM stage, but and needs that value when it enters the EX stage, which is when lw enters the MEM stage.
QTP: why can this situation not occur if the writing instruction is R-type?

## Slide 3: Handling a Load-Use Hazard
If we can stall the execution of the using instruction for one cycle:
- value to be loaded to $t2 will be available in the MEM/WB buffer when the using instruction moves from ID to EX
- that value can be forwarded to the using instruction as the using instruction enters the EX stage
lw $t2, 20($t1) # loads $t2
and $t4, $t2, $t5 # uses $t2
and STALL lw
A load-use hazard requires delaying the execution of the using instruction until the result from the loading instruction can be made available to the using instruction.

## Slide 4: Detection
When can we detect the existence of a load-use hazard?
When we are decoding the using instruction --- if we remember right information about the preceding instruction.
What do we need to remember?
- whether the preceding instruction reads a value from data memory
- whether the preceding instruction writes a value to the register file
- whether that value is written to a register that current instruction reads from
ID/EX.MemRead
ID/EX.RegisterRt
IF/ID.RegisterRs
IF/ID.RegisterRt
Why do we not need to consider this question?

## Slide 5: Load-Use Hazard Detection
The loading instruction must be just that… so it writes to register rt.
There is a load-use hazard when
ID/EX.MemRead AND
( ( ID/EX.RegisterRt == IF/ID.RegisterRs) OR
( ( ID/EX.RegisterRt == IF/ID.RegisterRt) )
If detected… do what?
1 iff we're executing a load instruction
ID/EX shows register being written to;
IF/ID shows registers being read from

## Slide 6: How to Stall the Pipeline
Force all control values in ID/EX register to 0
- when using reaches ID stage
- EX, MEM and WB do a nop
Prevent update of PC and IF/ID registers
- using instruction is decoded again
- instruction after the using instruction will be fetched again
- 1-cycle stall allows MEM to read data for lw
- can subsequently forward data to using instruction in EX stage
"If it isn't written down, it didn't happen."

## Slide 7: Trace
or and lw
lw $2, 20($1) # 1
and $4, $2, $5 # 2
or $8, $2, $6 # 3
add $9, $4, $2 # 4
When and reaches the ID stage, the hazard involving $2 is detected.
All the control signals from the ID stage are set to 0 and the PC and IF/ID interstage buffer are prevented from updating.

## Slide 8: Trace
or and STALL lw
Because IF/ID is not updated, the and instruction is processed through ID again.
Because PC is not updated, the or instruction is fetched again in the IF stage.
Resetting the control signals and locking PC and IF/ID cause:
And:
- EX operates as usual (with all relevant signals 0)
- EX sends only 0 control signals to MEM for the next cycle
lw reaches the MEM stage and reads the value to be written to $2.
That value goes into MEM/WB.

## Slide 9: Trace
add or and STALL lw
The control signals for and (set in ID in the previous cycle) reach EX.
The value for $2 in MEM/WB is forwarded to the ALU in EX.
Instructions preceding and proceed normally…
On the next cycle:
And:
- MEM operates as usual (with all relevant signals 0)
- MEM sends only 0 control signals to WB for the next cycle

## Slide 10: Stall/Bubble in the Pipeline
On the following cycles:
add or and STALL
add or and
… and so on…
The execution time has increased by one clock cycle.

## Slide 11: Simplified Datapath with Hazard Detection

## Slide 12: Stall Details
Zeroes all control signals iff Stall == 1
InhibitFetch == 1 locks buffer and PC
Stall == 1 iff load-use hazard

## Slide 13: Unsimplified Datapath with Hazard Detection
Yes:
add
sub
and
or
slt
sw
lw
No:
beq
j