## Slide 1: Transactional Memory: Architectural Support for Lock-Free Data Structures
Maurice Herlihy (DEC), J. Eliot & B. Moss (UMass)
Presenter: Mariano Diaz

## Slide 2: Part 1: Concepts and Hardware-based Approaches
Introduction
What’s a transaction?
Transaction: a finite sequence of machine instructions, executed by a single process, that satisfies the following:
  Serializability/Isolation
  Atomicity
Concept “borrowed” from databases..

## Slide 3: Introduction con’t
So what’s transaction memory?
Allows for concurrent, lock-free synchronization of shared memory using transactions on a multicore platform.
Why lock-free?
  Priority inversion
  Convoying
  Deadlock
  Nasty programming!..

## Slide 4: Introduction con’t
Approaches
  Hardware (faster, size-limitations, platform dependent)
  Software (slower, unlimited size, platform independent)
  Hybrid (common cases resolved in hardware, exceptions in software)
    Object-based (course-grained)
    Word-based (fine-grained)..

## Slide 5: Intended Use
To replace short critical sections.
Instructions for accessing memory:
  LT (Load-transactional)
  LTX (Load-transactional-exclusive)
  ST (Store-transactional)
Instructions to manipulate transaction state:
  Commit
  Abort
  Validate

## Slide 6: Intended Use con’t
Typical process:
  LT/ LTX to read from locations
  Validate
  ST to modify locations
  Commit
  If fail rinse and repeat
When contention is high, use adaptive backoff before retrying.

## Slide 7: Example

## Slide 8: Cache Implementation
What hardware are we working with?
Two types of cache:
  Regular
  Transactional
Shared Memory
Bus
address
value
state
tag
cache
. . .

## Slide 9: Cache Implementation con’t
Caches “snoop” on shared bus and react via cache coherence protocol. Since already built in, allows for free transaction conflict detection.
Cache coherence keeps the an address/value pair consistent across a set of caches.
Cache lines can be in either regular or transactional caches, both not both (same processor)..

## Slide 10: Line States
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Access | Shared? | Modified?
invalid | none | --- | ---
valid | R | yes | no
dirty | R, W | no | yes
reserved | R, W | no | no

## Slide 11: Transactional Tags
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Meaning
EMPTY | contains no data
NORMAL | contains committed data
XCOMMIT | discard on commit
XABORT | discard on abort

## Slide 12: Bus Cycles
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Kind | Meaning | New access
READ | regular | read value | shared
RFO | regular | read value | exclusive
WRITE | both | write back | exclusive
T_READ | transaction | read value | shared
T_RFO | transaction | read value | exclusive
BUSY | transaction | refuse access | unchanged

## Slide 13: Processor Flags
Processor maintains two flags:
  Transaction active (TACTIVE)
  Transaction status (TSTATUS)
TSTATUS indicates whether the transaction is active (True)
TACTIVE is set when first transactional operation is executed within transaction.
Used directly by Commit, Abort, Validate instructions.

## Slide 14: Scenarios
LT instruction
  If XABORT entry in transactional cache: return value
  If NORMAL entry
    Change NORMAL to XABORT
    Allocate second entry with XCOMMIT (same data)
    Return value
  Otherwise
    Issue T_READ bus cycle
      Successful: set up XABORT/XCOMMIT entries
      BUSY: abort transaction
LTX instruction
  Same as LT instruction except that T_RFO bus cycle is used instead and cache line state is RESERVED
ST instruction
  Same as LTX except that the XABORT value is updated

## Slide 15: Scenarios & Transaction States
Validate
  Returns TSTATUS flag
    False: set TACTIVE to False
        set TSTATUS to True
Abort
  Sets TSTATUS to True
  Sets TACTIVE to False
Commit
  Returns TSTATUS
  Sets TSTATUS to True
  sets TACTIVE to False

## Slide 16: Performance (Counting Benchmark)
TTS Lock
MCS Lock
QOSB
TM
LL/SC Direct