## Slide 1: Program Translation
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c)
Asm code (p1.s)
Object code (p1.o)
Executable program (p1)
Static libraries (.a)

## Slide 2: C Source to Assembly Code
C program (p1.c)
Asm code(p1.s)
.file "p1.c"
.text
.globl main
.type main, @function
main:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl $5, -4(%rbp)
movl $16, -8(%rbp)
movl -8(%rbp), %eax
movl -4(%rbp), %edx
addl %edx, %eax
movl %eax, -12(%rbp)
movl $0, %eax
leave
ret
. . .
// p1.c
int main() {
int x, y, t;
x = 5;
y = 16;
t = x + y;
return 0;
}
gcc –S –O0 -Wall –m64 p1.c
Notes: At this point, we are not concerned with the details of the assembly (or machine) representations. We just want to illustrate the multi-phase process of turning C source code into an executable.

## Slide 3: Assembly Code to Object Code
Asm code (p1.s)
.file "p1.c"
.text
.globl main
.type main, @function
main:
pushq %rbp
movq %rsp, %rbp
subq $16, %rsp
movl $5, -4(%rbp)
movl $16, -8(%rbp)
movl -8(%rbp), %eax
movl -4(%rbp), %edx
addl %edx, %eax
movl %eax, -12(%rbp)
movl $0, %eax
leave
ret
. . .
as –64 –o p1.o p1.s
55
89 e5
83 ec 10
c7 45 fc 05 00 00 00
c7 45 f8 10 00 00 00
8b 45 f8
8b 55 fc
8d 04 02
89 45 f4
b8 00 00 00 00
c9
c3
Object code (p1.o)

## Slide 4: Object Code to Executable
gcc -o p1 –m64 p1.o
x86 object (p1.o)
55
89 e5
83 ec 10
c7 45 fc 05 00 00 00
c7 45 f8 10 00 00 00
8b 45 f8
8b 55 fc
8d 04 02
89 45 f4
b8 00 00 00 00
c9
c3
Executable program (p1)
55
89 e5
53
83 ec 04
e8 00 00 00 00
5b
81 c3 74 1d 00 00
8b 93 fc ff ff ff
85 d2
74 05
e8 1e 00 00 00
e8 d5 00 00 00
e8 90 01 00 00
58
5b
c9
c3
. . .

## Slide 5: The Preprocessor
When a C compiler is invoked, the first thing that happens is that the code is parsed and modified by a preprocessor.
The preprocessor handles a collection of commands (commonly called directives), which are denoted by the character '#'.
#include directives specify an external file (for now a C library file); the preprocessor essentially copies the contents of the specified file in place of the directive.
We will see more interesting preprocessor directives later.
#include <stdio.h>
. . .
int main() {
printf("Hello, world!\n");
return 0;
}
Contents of file stdio.h are copied here.

## Slide 6: Typical C Program Organization
// single file
// a.h
// a.c
// b.h
// b.c
// z.h
// z.c
. . .
// main.c
For very small programs, code is often organized in a single source file; the most common convention uses the extension c for C source files.
For more interesting C programs, the code is typically organized into a collection of header files (extension h) and source files. In most cases, the header files contain only type declarations and function prototypes, while the c files contain the corresponding implementations.
#include directives are used within both h and c files to “import” declarations as necessary.
Notes: I use the term "module" to refer to a c/h pair, or more broadly to a collection of c/h files that define a coherent functional unit.

## Slide 7: Using Inclusion
#include directives are used within both h and cpp files to “import” declarations as necessary:
#include "A.h"
A(); // call
// A.h
#include <stdint.h>
uint64_t A();
// A.c
#include "A.h"
uint64_t A() {
// do stuff
}
// B.h
#include <stdint.h>
int32_t B(int32_t x);
// B.c
#include "B.h"
int32_t B(int32_t x) {
// do stuff
}
// main.c
#include "B.h"
int32_t x = B(42);
Notes: At this point, I'm taking more of a C++ view of linkage issues.
I'll talk about the details of external linkage later on; it would just muddy the waters at this point.

## Slide 8: Controlling Access
Often, a .c file includes some functions (and other things) that are needed only in that file:
// B.h
int32_t B(int32_t x);
// B.c
#include "B.h"
int32_t B(int32_t x) {
// do stuff
Helper();
}
void Helper() {
...
}
Here, B() calls Helper(), but no other functions outside of the file B.c do so…
So, we put the declaration of Helper() inside B.c, before any calls to it… and make it static…
… and we do NOT declare Helper() in B.h:
static void Helper();

## Slide 9: The Multiple Inclusion Problem
// main.c
#include "A.h"
#include "B.h"
It is possible to create some unfortunate situations:
Here, the preprocessor will copy the text of B.h into main.c twice, once due to the inclusion in A.h and once due to the explicit inclusion in main.c.
This scenario is difficult to avoid in large projects involving many individuals or teams.
However, there is a simple fix using preprocessor directives:
// A.h
#include "B.h"
// B.h
void foo();
// B.h
#ifndef B_H
#define B_H
void foo();
. . .
#endif
Notes: This often can happen when coalescing the pieces of a large system, where the pieces were implemented, and to some degree designed, by different developers.

## Slide 10: Example: Fibonacci
#include <stdio.h>
#include <inttypes.h>
#include "rFibonacci.h"
int main() {
for (int i = 0; i < 50; i++) {
printf("Fibo(%d) = %"PRIu64"\n", i, rFibonacci(i));
}
return 0;
}
Here's a short program with a test driver, a Fibonacci function in a second file, and a header file containing the declarations needed for the Fibonacci function:
#ifndef RFIBONACCI_H
#define RFIBONACCI_H
#include <stdint.h>
uint64_t rFibonacci(uint64_t n);
#endif
#include "rFibonacci.h"
uint64_t rFibonacci(uint64_t n) {
if ( n < 2 )
return 1;
return rFibonacci(n - 1) +
rFibonacci(n - 2);
}

## Slide 11: Compilation
#include <stdio.h>
#include <inttypes.h>
#include "rFibonacci.h"
int main() {
for (int i = 0; i < 50; i++) {
printf("Fibo(%d) = %"PRIu64"\n", i, rFibonacci(i));
}
return 0;
}
We can compile either c file without the other (but not produce an executable):
OK: the function call matches this declaration; compiler doesn't need to see function definition.
The compiler notes that this call "binds" to this declaration.
CentOS> gcc -o driver -std=c99 -Wall -W driver.c rFibonacci.c
CentOS> ls -l
total 24
-rwxrw-r--. 1 wmcquain comporg 8578 Sep 25 10:21 driver
-rw-rw-r--. 1 wmcquain comporg 216 Sep 25 10:19 driver.c
-rw-rw-r--. 1 wmcquain comporg 154 Sep 25 10:20 rFibonacci.c
-rw-rw-r--. 1 wmcquain comporg 104 Sep 25 10:20 rFibonacci.h
1029 wmcquain in ~/2505/notes/T08/v1>

## Slide 12: Compilation
CentOS> gcc -c -std=c99 -Wall -W driver.c
CentOS> ls -l
total 16
-rw-rw-r--. 1 wmcquain comporg 216 Sep 25 10:19 driver.c
-rw-rw-r--. 1 wmcquain comporg 1616 Sep 25 10:24 driver.o
-rw-rw-r--. 1 wmcquain comporg 154 Sep 25 10:20 rFibonacci.c
-rw-rw-r--. 1 wmcquain comporg 104 Sep 25 10:20 rFibonacci.h
-c switch tells gcc to compile and exit
If compilation is successful, an object file is created; this is a partial translation of the C source file into machine code.

## Slide 13: Linking
The final step in producing an executable is to invoke the linker.
The linker resolves the "notes" left by the compiler for external references (like the function name noted earlier), and writes the final executable file.
With gcc, the simplest way to do this is to just invoke gcc on the object files…

## Slide 14: Linking
CentOS> ls -l
total 20
-rw-rw-r--. 1 wmcquain comporg 216 Sep 25 10:19 driver.c
-rw-rw-r--. 1 wmcquain comporg 1616 Sep 25 10:24 driver.o
-rw-rw-r--. 1 wmcquain comporg 154 Sep 25 10:20 rFibonacci.c
-rw-rw-r--. 1 wmcquain comporg 104 Sep 25 10:20 rFibonacci.h
-rw-rw-r--. 1 wmcquain comporg 1424 Sep 25 10:26 rFibonacci.o
CentOS> gcc -o fibo -Wall -W driver.o rFibonacci.o
CentOS> ls -l
total 32
-rw-rw-r--. 1 wmcquain comporg 216 Sep 25 10:19 driver.c
-rw-rw-r--. 1 wmcquain comporg 1616 Sep 25 10:24 driver.o
-rwxrw-r--. 1 wmcquain comporg 8578 Sep 25 10:27 fibo
-rw-rw-r--. 1 wmcquain comporg 154 Sep 25 10:20 rFibonacci.c
-rw-rw-r--. 1 wmcquain comporg 104 Sep 25 10:20 rFibonacci.h
-rw-rw-r--. 1 wmcquain comporg 1424 Sep 25 10:26 rFibonacci.o
-o switch tells gcc what to call executable
can invoke gcc with object files to link them and produce executable

## Slide 15: Compilation Errors
#include <stdio.h>
#include <stdint.h>
#include <inttypes.h>
//#include "rFibonacci.h"
int main() {
for (int i = 0; i < 50; i++) {
printf("Fibo(%d) = %"PRIu64"\n", i, rFibonacci(i));
. . .
The compiler will generate error messages if it cannot resolve the references it encounters:
Omit this include directive and the compiler cannot find a declaration that matches the call to rFibonacci().
CentOS> gcc -c -std=c99 -Wall -W driver.c
driver.c: In function ‘main’:
driver.c:9:7: warning: implicit declaration of function ‘rFibonacci’ [-Wimplicit-function-declaration]
printf("Fibo(%d) = %"PRIu64"\n", i, rFibonacci(i));
^
driver.c:9:7: warning: format ‘%lu’ expects argument of type ‘long unsigned int’, but argument 3 has type ‘int’ [-Wformat=]

## Slide 16: Linker Errors
#include <stdio.h>
#include <stdint.h>
#include "rFibonacci.h"
int main() {
for (int i = 0; i < 50; i++) {
printf("Fibo(%d) = %lld\n", i, rFibonacci(i));
}
return 0;
}
The linker may also produce error messages:
#ifndef RFIBONACCI_H
#define RFIBONACCI_H
#include <stdint.h>
uint64_t rFibonacci(uint64_t n);
#endif
#include "rFibonacci.h"
uint64_t Fibonacci(uint64_t n) {
if ( n < 2 )
return 1;
return rFibonacci(n - 1) +
rFibonacci(n - 2);
}
OK
Now, linker cannot find a definition (implementation) that matches the function declaration the compiler matched the call to… that's an error.
Notes: Based on Chapter 1 in C++ for Java Programmers by Weiss

## Slide 17: Linker Errors
Unfortunately, linker error messages are less direct than compiler error messages:
The message does not refer to a specific line of source code.
But, it does name a specific function and it implies there's a difference between the declaration of that function and the definition (implementation) of that function.
CentOS> gcc -o driver -std=c99 -Wall -W driver.c rFibonacci.c
/tmp/ccHhmn0D.o: In function `main':
driver.c:(.text+0x1a): undefined reference to `rFibonacci'
/tmp/ccYcsMDA.o: In function `Fibonacci':
rFibonacci.c:(.text+0x27): undefined reference to `rFibonacci'
rFibonacci.c:(.text+0x3a): undefined reference to `rFibonacci'
collect2: error: ld returned 1 exit status

## Slide 18: Caesar Cypher Redux
// cypher.c
. . .
#include "caesar.h"
uint32_t processFile(int shiftAmt,
const char* const fileName);
. . .
int main(int argc, char** argv) {
. . .
}
. . .
uint32_t processFile(int shiftAmt,
const char* const fileName) {
. . .
}
. . .
The Caesar cypher program we saw earlier can be improved by separating the code that manages the input/output from the code that actually performs the translation:
// caesar.h
#ifndef CAESAR_H
#define CAESAR_H
#include <stdint.h>
char mapChar(char Original,
uint8_t shiftAmt);
#endif
// caesar.c
#include "caesar.h"
. . .
char mapChar(char Original,
uint8_t shiftAmt) {
. . .
}