## Slide 1: The von Neumann Machine
1945: John von Neumann
  Wrote a report on the stored program concept, known as the First Draft of a Report on EDVAC
  also Alan Turing… Konrad Zuse… Eckert & Mauchly…
The basic structure proposed in the draft became known as the “von Neumann machine” (or model).
  a memory, containing instructions and data
  a processing unit, for performing arithmetic and logical operations
  a control unit, for interpreting instructions

## Slide 2: The von Neumann Machine
Abstraction of von Neumann Architecture
decodes current instruction,
manages processing unit to carry out instruction
stores both program instructions and data
program counter: points to the next instruction to be fetched
instruction register: stores current instruction

## Slide 3: Intel x86 History
Totally dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!
    In terms of speed. Less so for low power.

## Slide 4: Intel x86 History
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit processor. Basis for IBM PC & DOS
  1MB address space
80386 1985 275K 16-33
  First 32 bit processor , referred to as IA32
  Added “flat addressing”
  Capable of running Unix
  32-bit Linux/gcc uses no instructions introduced in later models
Pentium 4F 2004 125M 2800-3800
  First 64-bit processor, referred to as x86-64
Core i7 2008 731M 2667-3333
  Our shark machines

## Slide 5: Intel x86 History
X86-64 / EM64t
X86-32/IA32
X86-16
8086
286
386
486
Pentium
Pentium MMX
Pentium III
Pentium 4
Pentium 4E
Pentium 4F
Core 2 Duo
Core i7
time
Architectures
Processors
MMX
SSE
SSE2
SSE3
SSE4

## Slide 6: Intel x86 History
Intel Attempted Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
AMD Stepped in with Evolutionary Solution
  x86-64 (now called “AMD64”)
Intel Felt Obligated to Focus on IA64
  Hard to admit mistake or that AMD's approach is better
2004: Intel Announces EM64T extension to IA32
  Extended Memory 64-bit Technology
  Almost identical to x86-64!
All but low-end x86 processors support x86-64
  But, lots of code still runs in 32-bit mode

## Slide 7: von Neumann View of x86
CPU
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes

## Slide 8: High-level x86 CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
CPU
PC
Registers
Condition
Codes

## Slide 9: IA32 Integer Registers
CPU
PC
Registers
Condition
Codes
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose

## Slide 10: x86-64 Integer Registers
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
  Extend existing registers. Add 8 new ones.
  Make %ebp/%rbp general purpose

## Slide 11: High-level x86 Memory
Memory
Object Code
Program Data
OS Data
Stack
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures

## Slide 12: Programming the Machine
But the hardware only "understands" binary representations
// C code
. . .
int imax(int first, int second) {
if ( first >= second )
return first;
return second;
}

## Slide 13: Programming the Machine
int imax(int first, int second) {
if ( first >= second )
return first;
return second;
}
457f464c010100010000000000000000
00010003000100000000000000000000
00bc0000000000000034000000000028
0009000689558be50845453b7c0c8b05
084503eb458b5d0c00c3000047004343
203a55287562746e2f75694c616e6f72
3420352e322e382d62756e7575742934
. . .
But who wants to program in binary?
gcc -O0 -c –m64 -std=c99 imax.c

## Slide 14: Programming the Machine
Solution:
translate high-level language code into intermediate-level code which is more human-friendly,
then translate that "assembly" code into the machine's langauge.
int imax(int first, int second) {
if ( first >= second )
return first;
return second;
}
. . .
imax:
pushq %rbp
movq %rsp, %rbp
subq $8, %rsp
movl %edi, -4(%rbp)
movl %esi, -8(%rbp)
movl -4(%rbp), %eax
cmpl -8(%rbp), %eax
jl .L4
movl -4(%rbp), %eax
jmp .L5
.L4:
movl -8(%rbp), %eax
.L5:
popq %rbp
ret
. . .

## Slide 15: Explanation: moving data
movl
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movl $0x4,%eax
tmp = 0x4;
movl $-147,(%rax)
*p = -147;
movl %eax,%edx
tmp2 = tmp1;
movl %eax,(%rdx)
*p = tmp;
movl (%rax),%edx
tmp = *p;
Src,Dest