## Slide 1: Credits and Disclaimers
The examples and discussion in the following slides have been adapted from a variety of sources, including:
Chapter 3 of Computer Systems 3nd Edition by Bryant and O'Hallaron
x86 Assembly/GAS Syntax on WikiBooks
(http://en.wikibooks.org/wiki/X86_Assembly/GAS_Syntax)
Using Assembly Language in Linux by Phillip ??
(http://asm.sourceforge.net/articles/linasm.html)
The C code was compiled to assembly with gcc version 4.8.3 on CentOS 7.
Unless noted otherwise, the assembly code was generated using the following command line:
gcc –S –m64 -fno-asynchronous-unwind-tables –mno-red-zone –O0 file.c
AT&T assembly syntax is used, rather than Intel syntax, since that is what the gcc tools use.

## Slide 2: Shift Instructions
Shifting the representation of an integer
sall rightop, leftop
leftop = leftop << rightop // C syntax!
sarl rightop, leftop
leftop = leftop >> rightop (preserves sign)
shll rightop, leftop
leftop = leftop << rightop (same as sall)
shrl rightop, leftop
leftop = leftop >> rightop (hi bits set to 0)

## Slide 3: Left Shifts and Multiplication
Shifting an integer operand to the left by k bits is equivalent to multiplying the operand's value by 2k:
sall 1, %eax # eax = 2*eax
sall 3, %edx # edx = 8*edx
For example:
Since general multiplication is much more expensive (in time) than shifting bits, we should prefer using a shift-left instruction when multiplying by a power of 2.
edx | 00000000 00000000 00000000 00000101 | 5
edx | 00000000 00000000 00000000 00101000 | 40

## Slide 4: Right Shifts, Unsigned Operands, and Division
Shifting an integer operand to the right by k bits might be expected to divide the operand's value by 2k:
shrl 1, %eax # eax = eax / 2 ?
Recall that shrl shifts in 0's on the left; so this will indeed perform integer division by 2, provided the value in eax is interpreted as an unsigned integer.
For example, if we have an 8-bit unsigned representation of 25510, the instruction above would perform the following transformation:
1111 1111  0111 1111
So it would yield 12710, which is correct for integer division.

## Slide 5: Right Shifts, Unsigned Operands, and Division
But, the following will not yield the correct result for an unsigned integer:
sarl 1, %eax # eax != eax / 2
For example, if we consider an 8-bit representation of 20010, the instruction above would produce this transformation:
1100 1000  1110 0100
So it would yield 22810, which is incorrect.
The correct result would be 10010 which would be represented as 0110 0010.
Note that the correct value would have been found by using shrl instead.

## Slide 6: Right Shifts, Signed Operands, and Division
Shifting a non-negative (signed) integer operand to the right by k bits will divide the operand's value by 2k:
shrl 1, %eax # eax = eax / 2
sarl 1, %eax # eax = eax / 2
If eax holds a non-negative signed integer, the left-most bit will 0, and so both of these instructions will yield the same result.
But, if the signed operand is negative, then the high bit will be 1.
Clearly, shrl cannot yield the correct quotient in this case. Why?

## Slide 7: Right Shifts, Signed Operands, and Division
What about the following instruction, if eax holds a negative signed value?
sarl 1, %eax # eax = eax / 2
sarl replicates the sign bit, so this will yield a negative result…
But, suppose we have an 8-bit representation of -7: 1111 1001
Then applying an arithmetic right shift of 1 position yields: 1111 1100
That represents the value -4… is that correct?
Mathematics says yes by the Division Algorithm:
-7 = -4 * 2 + 1
Remainders must be >= 0!
C says no:
-7 = -3 * 2 + -1
-7 % 2 must equal -(7 % 2)

## Slide 8: Logical Instructions
There are the usual logical operations, applied bitwise:
andl rightop, leftop
leftop = leftop & rightop // C syntax!
orl rightop, leftop
leftop = leftop | righttop
xorl rightop, leftop
leftop = leftop ^ rightop
notl op
op = ~op

## Slide 9: Arithmetic/Logic Example
int arith(int x, int y, int z) {
. . .
}
 | . . .
rbp | old value of rbp
rsp | . . .
the Stack
frame for caller
fame for arith()
Calling a function causes the creation of a stack frame dedicated to that function.
The frame pointer register, rbp,
points to the beginning of the stack frame for the currently-running function.
The stack pointer register, rsp, points to the last thing that was pushed onto the stack.
(As an optimization, %rsp may or may not actually be updated. More on this later).

## Slide 10: Arithmetic/Logic Example
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
 | . . .
rbp + 8 | return address
rbp | old value of rbp
rbp – 4 | t1
rbp – 8 | t2
rbp - 12 | t3
rbp - 16 | t4
rbp - 20 | x
rbp - 24 | y
rbp – 28 | Z
the Stack
autos within fn
The first 6 function arguments are passed in registers, additional arguments are passed on the stack.
The arguments stored in registers are often moved somewhere else on the stack before any computations.
In this example:
x is passed in register %edi and is moved to -20(%rbp).
y is passed in register %esi and is moved to -24(%rbp).
z is passed in register %edx and is moved to -28(%rbp).

## Slide 11: Arithmetic/Logic Example
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
  Mapping:
  address
  x rbp – 20
  y rbp - 24
  t1 rbp - 4
movl -24(%rbp), %eax # eax = y
movl -20(%rbp), %edx # edx = x
addl %edx, %eax # eax = x + y
movl %eax, -4(%rbp) # t1 = x + y

## Slide 12: Arithmetic/Logic Example
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
  Mapping:
  address
  z rbp - 28
  t2 rbp - 8
movl -28(%rbp), %edx # edx = z
movl %edx, %eax # eax = z
addl %eax, %eax # eax = z + z = 2z
addl %edx, %eax # eax = 2z + z = 3z
sall $4, %eax # eax = (3z) << 4 = 3z*16 = 48z
movl %eax, -8(%rbp) # t2 = 48z

## Slide 13: Arithmetic/Logic Example
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
  Mapping:
  address
  t1 rbp - 4
  t3 rbp - 12
movl -4(%rbp), %eax # eax = t1
movzwl $ax, %eax # eax = t1 & 0xFFFF
movl %eax, -12(%rbp) # t3 = t1 & 0xFFFF

## Slide 14: Aside: movzwl
You may have noticed the movzwl instruction:
. . .
movzwl $ax, %eax # eax = t1 & 0xFFFF
. . .
This moves a zero extended (z) word (16 bits) stored in %ax to %eax.
And is equivalent to t1 & 0xFFFF since that will zero out the high 16 bits in %eax preserving the rest.
We'll see other versions of this instruction later. There are different sizes (movzb) and there’s are signed variants (movsb).
In this case, movzwl apparently offered a performance (or some other) advantage.

## Slide 15: Arithmetic/Logic Example
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
  Mapping:
  address
  t2 rbp - 8
  t3 rbp - 12
  t4 rbp - 16
movl -8(%rbp), %eax # eax = t2
imull -12(%rbp), %eax # eax = t2 * t3
movl %eax, -16(%rbp) # t4 = t2 * t3

## Slide 16: Assembled Code
.file "arith.c"
.text
.globl arith
.type arith, @function
arith:
pushq %rbp # save old frame pointer
movq %rsp, %rbp # move frame pointer to top
movl %edi, -20(%rbp) # move arguments x, y, and z
movl %esi, -24(%rbp)
movl %edx, -28(%rbp)
. . .
movl -16(%rbp), %eax # set return value in eax
popq %rbp # rsp = rbp; pop to rbp
ret # return to caller
.size arith, .-arith
.ident "GCC: (GNU) 4.8.3 20140911 ..."
.section .note.GNU-stack,"",@progbits
int arith(int x, int y, int z) {
. . .
int t4 = t2 * t3;
return t4;
}
gcc –O0 -S -Wall -m32 arith.c

## Slide 17: Assembled Code
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
. . .
movl -24(%rbp), %eax # eax = y
movl -20(%rbp), %edx # edx = x
addl %edx, %eax # eax = x + y
movl %eax, -4(%rbp) # t1 = x + y
movl -28(%rbp), %edx # edx = z
movl %edx, %eax # eax = z
addl %eax, %eax # eax = z + z = 2z
addl %edx, %eax # eax = 2z + z = 3z
sall $4, %eax # eax = (3z) << 4 = 3z*16 = 48z
movl %eax, -8(%rbp) # t2 = 48z
. . .
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
. . .
}

## Slide 18: Assembled Code
int arith(int x, int y, int z) {
int t1 = x + y;
int t2 = z*48;
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
return t4;
}
. . .
movl -4(%rbp), %eax # eax = t1
movzwl %ax, %eax # eax = t1 & 0xFFFF
movl %eax, -12(%rbp) # t3 = t1 & 0xFFFF
movl -8(%rbp), %eax # eax = t2
imull -12(%rbp), %eax # eax = t2 * t3
movl %eax, -16(%rbp) # t4 = t2 * t3
. . .
int arith(int x, int y, int z) {
. . .
int t3 = t1 & 0xFFFF;
int t4 = t2 * t3;
. . .
}