## Slide 1: Logic Design
Goal: to become literate in most common concepts and terminology of digital electronics
Important concepts:
- use abstraction and composition to implement complicated functionality with very simple digital electronics
- keep things as simple, regular, and small as possible
Things we will not explore:
- physics
- chip fabrication
- layout
- tools for chip specification and design

## Slide 2: Motivation
Consider the external view of addition:
What kind of circuitry would go into the "black box" adder to produce the correct results?
How would it be designed? What modular components might be used?
Adder
???
x + y
y
x
Error?

## Slide 3: Basic Logic Gates
Fundamental building blocks of circuits; mirror the standard logical operations:
OR gate
AND gate
NOT gate
A | Out
0 | 1
1 | 0
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Note the outputs of the AND and OR gates are commutative with respect to the inputs.
Multi-way versions of the AND and OR gates are commonly assumed in design.

## Slide 4: Additional Common Logic Gates
NAND gate
XOR gate
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NOR gate
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
XNOR gate
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5: Combinational and Sequential Circuits
A combinational circuit is one with no "memory". That is, its output depends only upon the current state of its inputs, and not at all on the current state of the circuit itself.
A sequential circuit is one whose output depends not only upon the current state of its inputs, but also on the current state of the circuit itself.
For now, we will consider only combinational circuits.

## Slide 6: From Function to Combinational Circuit
Given a simple Boolean function, it is relatively easy to design a circuit composed of the basic logic gates to implement the function:
This circuit implements the exclusive or (XOR) function, often represented as a single logic gate:

## Slide 7: Sum-of-Products Form
A Boolean expression is said to be in sum-of-products form if it is expressed as a sum of terms, each of which is a product of variables and/or their complements:
It's relatively easy to see that every Boolean expression can be written in this form.
Why?
The summands in the sum-of-products form are called minterms.
- each minterm contains each of the variables, or its complement, exactly once
- each minterm is unique, and therefore so is the representation (aside from order)

## Slide 8: Sum-of-Products Form
Given a truth table for a Boolean function, construction of the sum-of-products representation is trivial:
- for each row in which the function value is 1, form a product term involving all the variables, taking the variable if its value is 1 and the complement if the variable's value is 0
- take the sum of all such product terms
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 9: Equivalence

## Slide 10: Efficiency of Expression
While the sum-of-products form is arguably natural, it is not necessarily the simplest way form, either in:
- number of gates (space)
- depth of circuit (time)

## Slide 11: 1-bit Half Adder
Let's make a 1-bit adder (half adder)… we can think of it as a Boolean function with two inputs and the following defining table:
A | B | Sum
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Here's the resulting circuit.
It's equivalent to the XOR circuit seen earlier.
But… in the final row of the truth table above, we've ignored the fact that there's a carry-out bit.

## Slide 12: Dealing with the Carry
The carry-out value from the 1-bit sum can also be expressed via a truth table.
However, the result won't be terribly useful unless we also take into account a carry-in.
A | B | Cin | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
The resulting sum-of-products expressions are:

## Slide 13: 1-bit Full Adder
The expressions for the sum and carry lead to the following unified implementation:

## Slide 14: 1-bit Full Adder as a Module
When building more complex circuits, it is useful to consider sub-circuits as individual, "black-box" modules. For example:

## Slide 15: Chaining a 4-bit Adder
An 4-bit adder built by chaining 1-bit adders:
This has one serious shortcoming. The carry bits must ripple from top to bottom, creating a lag before the result will be obtained for the final sum bit and carry.

## Slide 16: Carry-Lookahead Adder
Perhaps surprisingly, it's possible to compute all the carry bits before any sum bits are computed... and that leads to a faster adder design:
Why is this faster than the ripple-carry approach?

## Slide 17: Latency
The answer lies in the concept of gate latency.
Each logic gate takes a certain amount of time (usually measured in picoseconds) to stabilize on the correct output... we call that the latency of the gate.
For simplicity, we'll assume in this course that all gates (except inverters) have the same latency, and that inverters are so fast they can be igored.
Then, the idea is that the latency of a circuit can be measured by the maximum number of gates a signal passes through within the circuit... called the depth of the circuit.
So, the 1-bit full adder we saw earlier has a depth of 2.

## Slide 18: Carry-Lookahead Adder Latency
Without going into details:
How does that compare to the ripple-carry approach?
Depth is 3 gates
Depth is 2 gates
Total depth is 5 gates

## Slide 19: Ripple-carry Latency
A 4-bit ripple-carry design would have 4 1-bit full adders, and we've seen that each of those has a depth of 2 gates.
But those adders fire sequentially, so running one after the other would entail a total depth of 8 gates.
So, the ripple-carry design would be 1.6 times as "deep" and it's not unreasonable to say it would take about 1.6 times as long to compute the result.
Just how you'd implement the computation of those carry bits is an interesting question...

## Slide 20: Refined Adder Design
The following slides illustrate an approach used to improve efficiency, versus the ripple-carry design covered earlier.
These may or not be covered, at the discretion of your instructor.

## Slide 21: Carry-Lookahead Logic
Let's look at just how the carry bits depend on the summand bits:
c4 c3 c2 c1 c0
a3 a2 a1 a0
b3 b2 b1 b0
-------------
s3 s2 s1 s0
It's clear that c1 = 1 if and only if at least two of the bits in the previous column are 1.
Since this relationship holds for every carry bit (except c0), we have the following general Boolean equation for carry bits:
We will allow for a carry-in in the low-order position (c0).
(Note that • represents AND and + represents OR.)
Notes: I'd say the discussion of the carry-lookahead adder is an "extra". It's interesting, if time permits, but it's not essential.

## Slide 22: Carry-Lookahead Logic
Now, this relationship doesn't seem to help until we look at it a bit more deeply:
If we define
then we get the following relationships:
Now, we can calculate all of the gi and pi terms at once, from the bits of the two summands, and c0 will be given, so we can compute c1 and c2 before we actually do the addition!

## Slide 23: Carry-Lookahead Logic
Finally, here's how we can calculate c3 and c4:
So, we have the necessary logic to implement the 4-bit Carry Lookahead unit for our 4-bit Carry Lookahead Adder:

## Slide 24: Carry-Lookahead Logic

## Slide 25: Abstraction
The gi and pi bits represent an abstract view of how carry bits are generated and propagate during addition:
generate bit for i-th column
adding the summand bits generates a carry-out bit iff both summand bits are 1
propagate bit for i-th column
if ci = 1 (the carry-out bit from the previous column), there's a carry-out into the next column iff at least one of the summand bits is 1

## Slide 26: Abstraction
So, here's why the formulas we've derived make sense intuitively:
c1 is 1 iff:
c0 was 1 and column 0 propagated it
or
column 0 generated a carry-out
c4 is 1 iff:
c0 was 1 and columns 0 to 3 propagated it, or
column 0 generated a carry-out and columns 1 to 3 propagated it, or
column 1 generated a carry-out and columns 2 to 3 propagated it, or
column 2 generated a carry-out and column 3 propagated it, or
column 3 generated a carry-out

## Slide 27: Implementation Below the Gate Level
The following slides illustrate how transistors might be used to implement the logic gates introduced earlier.
These may or not be covered, at the discretion of your instructor.

## Slide 28: Aside: Transistors
Transistors are a primary building block for electronic circuits.
* By Brews ohare - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=18796795
MOS-FET
(metal-oxide-semiconductor field-effect transistor)
Mohamed Atalla & Dawon Kahng, Bell Labs
gate input
source
drain
base
insulator
1953
1959
Notes: This is NOT mandatory, but it may shed some further light on how things really work.

## Slide 29: Aside: Transistors
gate input
source
drain
base
insulator
P-type transistor
gate input 0: source is sent to drain
gate input 1: drain is "floating"
N-type transistor
gate input 0: drain is "floating"
gate input 1: source is sent to drain
Notes: This is NOT mandatory, but it may shed some further light on how things really work.

## Slide 30: Aside: Implementing Logic Gates
Here's one way an inverter might be implemented:
(Apologies to electronics engineers for the inherent imprecision of this.)
data input
source
Output signal equals complement of data input.
P-type transistor
gate input 0: source is sent to drain
gate input 1: drain is "floating"
drain
Pull resistor
(reduces signal that's less than 1 to 0)
gate
Notes: This is NOT mandatory, but it may shed some further light on how things really work.

## Slide 31: Aside: Implementing Logic Gates
Here's one way an AND gate might be implemented:
(Apologies to electronics engineers for the inherent imprecision of this.)
data input
source
Output signal equals AND of data inputs
N-type transistor
gate input 0: drain is "floating"
gate input 1: source is sent to drain
drain
Pull resistors
data input
gate

## Slide 32: Aside: Implementing Logic Gates
Here's one way an OR gate might be implemented:
(Apologies to electronics engineers for the inherent imprecision of this.)
data input
source
Output signal equals OR of data inputs
N-type transistor
gate input 0: drain is "floating"
gate input 1: source is sent to drain
drain
Pull resistor
gate
data input