## Slide 1: Hardware Level Organization
PC
IR
Ex Unit
CPU
I/O Module
buffers
Main Memory
Instruction
Instruction
Instruction
Data
Data
Data
0
n-1
System
Bus
PC = program counter
IR = instruction register
Major components:
- memory
- central processing unit
- registers
- the fetch/execute cycle
(the hardware process)
Arithmetic/Logic
Registers
Instr Decoding

## Slide 2: Central Processing Unit
Control
- decodes instructions and manages CPU’s internal resources
Registers
- general-purpose registers available to user processes
- special-purpose registers directly managed in fetch/execute cycle
- other registers may be reserved for use of operating system
- very fast and expensive (relative to memory)
- hold all operands and results of arithmetic instructions (on RISC systems)
- save bits in instruction representation
Data path or arithmetic/logic unit (ALU)
- operates on data

## Slide 3: Stored Program Concept
memory for data, programs,
compilers, editors, etc.
Fetch & Execute Cycle
  Instructions are fetched and put into a special register
  Bits in the register "control" the subsequent actions
  Fetch the “next” instruction and continue
Instructions are collections of bits
Programs are stored in memory, to be read or written just like data
PC
MAR
IR
MBR
I/O AR
I/O BR
Ex Unit
CPU
Main Memory
Instruction
Instruction
Instruction
Data
Data
Data
0
n-1

## Slide 4: Stored Program Concept
Of course, on most systems several programs will be stored in memory at any given time.
On most contemporary systems instructions of only one of those will be executed at any given instant.
The operating system will rapidly switch among the eligible processes, producing the illusion that several programs are executing at the same time.
PC
MAR
IR
MBR
I/O AR
I/O BR
Ex Unit
CPU
Main Memory
PowerPoint pgm
(machine code)
vim
(machine code)
GIS source code
(data)
g++
(machine code)

## Slide 5: Fetch/Execute Cycle
Sometimes called the hardware process… executes continuously.
Steps:
- fetch an instruction from memory to the instruction register
- increment the program counter register (by the instruction length)
- decode the instruction (in the control unit)
- fetch operands, if any, usually from registers
- perform the operation (in the data path); this may modify the PC register
- store the results, usually to registers
Fetch Stage
Execute Stage
Fetch Next Instruction
Execute Instruction
START
HALT

## Slide 6: Machine Language
But, how is all of this driven?
Machine language:
- registers store collections of bits
- all data and instructions must be encoded as collections of bits (binary)
- bits are represented as electrical charges (more or less)
- control logic and arithmetic operations are implemented as circuits, which are driven by the movement of electrical charges
- so, the instructions directly manipulate the underlying hardware (cool, huh?)
The collection of all valid binary instructions is known as the machine language.
- what’s valid depends on the design of the hardware, especially the control circuitry
- must be formally specified
- machine language is not human-friendly

## Slide 7: Assembly Language
More human-friendly syntax:
- expressed in text, not in binary
- instructions are identified by (more-or-less) mnemonic names
- instruction operands may include registers, memory locations, or…
Aspects of assembly language:
- unlike high-level languages, each instruction is extremely simple, so assembly language programs are much longer than corresponding high-level language programs
- assembly language must be translated into machine language in order to be executed
- assembly language is not usually any more portable across different hardware platforms that is machine language
- most assembly languages are quite similar… from a certain point of view

## Slide 8: MIPS ISA
We’ll be working with the MIPS instruction set architecture (ISA)
- similar to other architectures developed since the 1980's
- almost 100 million MIPS processors manufactured in 2002
- used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, …

## Slide 9: MIPS Registers
Registers
- 32 32-bit general-purpose registers, referred to as $0, $1, …, $31
- 32 32-bit floating-point registers, referred to as $f0, $f1, … $f31
- 16 64-bit floating-point registers, referred to as $f0, $f2, … $f30
- conventions govern the use of the general registers
We will, for now, adopt the view that the underlying computer is a “black box” that understands MIPS machine language.

## Slide 10: Registers vs. Memory
Operands to arithmetic and logical instructions must be registers or immediates.
Compiler associates variables with registers
What about programs with lots of variables?
Processor
I/O
Control
Datapath
Memory
Input
Output

## Slide 11: MIPS Assembly Language
We will study the MIPS assembly language as an exemplar of the concept.
MIPS assembly instructions each consist of a single token specifying the command to be carried out, and zero or more operation parameters:
<mnemonic> par1 par2 … parN
The tokens are separated by commas. Indentation is insignificant to the assembler, but is certainly significant to the human reader.
MIPS command tokens are short and mnemonic (in principle). For example:
add lw sw jr

## Slide 12: MIPS Assembly Language
MIPS operands include:
- hardware registers
- offset and base register
- literal constants (immediate parameters)
- labels
There are also some special directives, but those can wait...
Of course, MIPS assembly also allows comments. Simply, all characters from a ‘#’ character to the end of the line are considered a comment.

## Slide 13: Memory Organization
Viewed as a large, single-dimension array, with an address.
A memory address is an index into the array
"Byte addressing" means that the index points to a byte of memory.
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 14: MIPS Memory Organization
Bytes are nice, but most data items use larger "words"
For MIPS, a word is 32 bits or 4 bytes.
0
4
8
12
...
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Registers hold 32 bits of data
232 bytes with byte addresses from 0 to 232 - 1
230 words with byte addresses 0, 4, 8, ... 232 - 4
Words are aligned, that is, each has an address that is a multiple of 4.
MIPS can be either big-endian (that is, the address of each word is the address of the “left-most” byte of the word) or little-endian. This is important when viewing the contents of memory.

## Slide 15: Simple MIPS Overview
http://jamesgart.com/procsim/