## Slide 1: Machine Language
Of course, the hardware doesn’t really execute MIPS assembly language code.
The hardware can only store bits, and so the instructions it executes must be expressed in a suitable binary format.
We call the language made up of those instructions the machine language.
Different families of processors typically support different machine languages.
In the beginning, all programming was done in machine language… very ugly…
Assembly languages were created to make the programming process more human-centric.
Assembly language code is translated into machine language by an assembler.
Alas, there is no universal assembly language. In practice, assembly languages are tightly coupled with the underlying machine language and hardware.

## Slide 2: Assembly Language vs. Machine Language
Assembly provides convenient symbolic representation
- much easier than writing down numbers
- e.g., destination first
Machine language is the underlying reality
- e.g., destination is no longer first
Assembly can provide 'pseudoinstructions'
- e.g., “move $t0, $t1” exists only as an extension to assembly
- would be translated to “add $t0,$t1,$zero” by the assembler
When considering performance you should count real instructions

## Slide 3: Classifying the Assembly Instructions
Examining the (basic) MIPS assembly instructions, we can easily identify three fundamentally different categories, according to the parameters they take:
- instructions that take 3 registers
add $s0, $s1, $s2
or $t1, $t0, $t1
- instructions that take 2 registers and an immediate (offset, number, address, etc.)
addi $t7, $s5, 42
lw $s3, 12($t4)
beq $t1, $t3, Label01
- instructions that take an immediate
j Label01

## Slide 4: Overview of MIPS Machine Language
Simple instructions, all 32 bits wide
Very structured, no unnecessary baggage
Only three* instruction formats with strictly-defined fields:
R-format: basic arithmetical-logical instructions
I-format load/store/conditional branch instructions
J-format: jump/unconditional branch instructions
R
funct
shamt
rd
rt
rs
op
16-bit immediate
rt
rs
op
26-bit immediate
op
I
J
* Well… not really…

## Slide 5: Overview of MIPS Machine Language
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises

## Slide 6: Overview of MIPS Machine Language
R
funct
shamt
rd
rt
rs
op
16-bit immediate
rt
rs
op
26-bit immediate
op
I
J
In MIPS32 Release 2, there are over 200 basic MIPS machine instructions.
In order to specify that many different instructions, we could use a field of 7 or more bits in every machine instruction.
But MIPS machine language uses a 6-bit opcode field and a variety of special cases.
For R-format instructions, the opcode field is set to 000000, and the last 6 bits specify exactly which arithmetic/logical instruction is to be performed.

## Slide 7: Arithmetic/Logical Instructions
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t1, $s1, $s2
  registers have numbers, $t1 = 9, $s1 = 17, $s2 =18
Machine language basic arithmetic/logic instruction format:
100000
00000
01001
10010
10001
000000
funct
shamt
rd
rt
rs
op
Can you guess what the field names stand for?
op operation code (opcode)
rs 1st source register
rt 2nd source register
rd destination register
shamt shift amount
funct opcode variant selector
Notes: Board work: Binary Numbers

## Slide 8: Mapping Assembly to Machine Language
Note how the assembly instruction maps into the machine representation:
  add $t1, $s1, $s2
100000
00000
01001
10010
10001
000000
funct
shamt
rd
rt
rs
op
The three register fields are each 5 bits wide. Why?
For arithmetic-logical instructions, both the op field and the funct field are used to specify the particular operation that is to be performed.
If you view memory contents, this would appear as 0x02324820.
Notes: Board work: Binary Numbers

## Slide 9: Load Instructions
Consider the load-word and store-word instructions:
- what would the regularity principle have us do?
- new principle: Good design demands a compromise
We need a different type of machine language instruction format for these:
- I-type for data transfer instructions
- other format was R-type for register
Example: lw $t0, 32($s2)
0000 0000 0010 0000
01000
10010
100011
16-bit number
rt
rs
op
Where's the compromise?

## Slide 10: Jump Instructions
Consider the jump instruction: j Label01
We need a different type of machine language instruction format for this as well.
Example: j exit # assume exit is a statement label
26-bit offset depending on value of exit
000010

## Slide 11: Anticipating Execution
What will be involved in executing a machine language instruction?
Consider an I-type instruction, say a lw instruction:
16-bit immediate
rt
rs
op
I
The opcode bits must be analyzed to determine that the instruction is lw.
The contents of $rs must be fetched to the ALU and added to the immediate field to compute the appropriate address.
The contents at that address must be fetched from memory and written to register $rt.
Notes: 11