## Slide 1: Introduction
We will examine a simplified MIPS implementation first, and then produce a more realistic pipelined version.
A simple, representative subset of machine instructions, shows most aspects:
- Memory reference: lw, sw
- Arithmetic/logical: add, sub, and, or, slt
- Transfer of control: beq, j
R
funct
shamt
rd
rt
rs
op
16-bit immediate
rt
rs
op
26-bit immediate
op
I
J
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 2: Instruction Execution
I PC  instruction memory, fetch instruction
II Register numbers  register file, read registers to get operand(s)
III Depending on instruction class
- May use ALU to calculate needed value
- R-type: need result of specified operation
- Load/store: need memory address to be read from/written to
- Branch: need to compare registers AND need the branch target address
- May access data memory
- Load/store: access data memory to read/write value
- Set address for next instruction fetch: PC  branch target OR PC + 4 OR jump target

## Slide 3: Executing Instruction Fetch
Here's what we need for sequential fetches (no beq or j):
32-bit register storing address of instruction to fetch next
increment by 4 for next instruction (for now)
assume there are separate storage for instructions and data (for now)

## Slide 4: Executing R-Format Instructions
funct
shamt
rd
rt
rs
op
Register
numbers
Operation
results
Register file
Operands
Read two operands from register file
Use ALU to perform the arithmetic/logical operation
Write the result to a register
Control
GPR[rd] = GPR[rs] funct GPR[rt]

## Slide 5: Executing R-Format Instructions
funct
shamt
rd
rt
rs
op
rs and rt specify where operands are
rd specifies where result goes
ALU applies specified operation to operands
ALU Control sets ALU to correct operation
add, sub, and, or, slt
ALU result goes to register file
GPR[rd] = GPR[rs] funct GPR[rt]
Control tells ALU Control to use the funct bits… and sets RegWrite to 1

## Slide 6: Executing Load Instructions
Read register operand
Calculate the address to be read using register operand and 16-bit offset from instruction
- Use ALU, but sign-extend offset
. . .
16-bit immediate
rt
rs
op
GPR[rt] = Mem[GPR[rs] + imm]

## Slide 7: Executing Load Instructions
16-bit immediate
rt
rs
op
. . .
Read memory and update register
GPR[rt] = Mem[GPR[rs] + imm]

## Slide 8: Executing Load Instructions
16-bit immediate
rt
rs
op
rs specifies where operand is
16-bit immediate is extended
rt specifies where result goes
lw
GPR[rt] = Mem[GPR[rs] + imm]
Control tells ALU Control to add operands and sets RegWrite to 1 and MemRead to 1
Value is retrieved from memory location and sent to register file
ALU computes address to read

## Slide 9: Executing Store Instructions
16-bit immediate
rt
rs
op
rs specifies where operand is
16-bit immediate is extended
rt specifies where data comes from
sw
Mem[GPR[rs] + imm] = GPR[rt]
Control tells ALU Control to add operands, and sets MemWrite to 1
ALU computes address to read
Value is retrieved from register file and sent to memory

## Slide 10: Unifying the Designs
In order to produce a complete datapath design, we must identify and deal with any conflicts.
First, consider the specification of the register numbers supplied to the register file.
They come from the current instruction, but using which bits?
 | Read reg 1 | Read reg 2 | Write reg
R-type | 25:21 | 20:16 | 15:11
load | 25:21 | not used | 20:16
store | 25:21 | 20:16 | not used
We have a conflict regarding the write register.
To resolve the conflict, we must be able to select one set of bits for R-type instructions and a different set of bits for the load instructions… how do we make a selection in hardware?
OK
OK
Conflict

## Slide 11: Unifying the Designs
We also have a conflicts regarding the source of the write data and the source of the right (lower) operand to the ALU:
 | Write data source | Right operand source
R-type | ALU output | register file
load | Data memory | sign-extend
store | not used | sign-extend
To resolve these conflicts, we must be able to:
- send the ALU output to the register file for R-type instructions, but send the data read from the memory unit to the register file for load instructions
- send the data read from the register file to the ALU for R-type instructions, but send the output from the sign-extender to the ALU for load and store instructions
Conflict
Conflict

## Slide 12: Unified R-type/Load/Store Datapath
By adding three multiplexors, we can resolve the conflicts that we have identified and produce a design that will (almost) handle the R-type, load and store instructions we are considering.
Multiplexor to select write register number
Multiplexor to select right operand to ALU
Multiplexor to select write data for register file
add, sub, and, or, slt, lw, sw

## Slide 13: Analyzing the Control Signals
We've identified quite a few necessary control signals in our design.
Which ones are two-valued? Do any require more than two values?
How should they be set?
The datapath cannot operate correctly unless every control signal is managed properly.
Two things to remember:
- Every line always carries a value. We may not know (or care) what it is in some cases. But there is always a value there.
- It doesn't matter what value a line carries if that value is never stored or used to make a decision. (Hence, we will find that we have don't-care conditions.)

## Slide 14: Register File Control
R-type and load instructions require writing a value into a register, but the store instruction does not.
Writing a value modifies the state of the system, so it is not a don't-care.
So, we must manage the RegWrite signal accordingly:
 | RegWrite
R-type | 1
load | 1
store | 0
Value at Write data is written to the Write register iff RegWrite is 1.

## Slide 15: Data Memory Control
MemRead
- must be 1 for load instructions, since they copy a value from memory to a register
- might be a don't-care for R-type and store instructions… why? If not, should be 0.
MemWrite
- must be 1 for store instructions, since they copy a value from a register to memory
- must be 0 for R-type and load instructions; otherwise they could modify a memory value that should not be changed
 | MemRead | MemWrite
R-type | ? | 0
load | 1 | 0
store | ? | 1

## Slide 16: Multiplexor Control
RegDst
- must be 0 for load instructions
- must be 1 for R-type instructions
- don't-care for store instructions (why?)
see slide 10
see slide 11
see slide 15
ALUSrc
- must be 0 for R-type instructions
- must be 1 for load and store instructions
MemtoReg
- must be 1 for load instructions
- must be 0 for R-type instructions
- don't-care for store instructions (why?)

## Slide 17: ALU Control
There are a lot of control signals, even in our simple datapath.
At this point, almost all of them are single-bit signals (i.e., they make a choice between two alternate actions).
The ALU control needs to be different because there are more than two choices for what it will actually do:
 | ALU
R-type add sub and or slt | add subtract and or slt
load | add
store | add
So, the ALU will require a multi-bit control signal… why? How many bits?

## Slide 18: ALU Control
This suggests separating the control logic into two modules:
- a master control module that determines the type of instruction being executed and sets the non-ALU control signals
- a secondary control module that manages the interface of the ALU itself
The master module will send :
- a specific selector pattern for the ALU if the instruction is not R-type; e.g., it sends the ADD selector pattern for lw and sw instructions
- a flag telling the secondary module to analyze the funct bits if the instruction is R-type
We'll fill in the details of the two modules later, but for now we do know what each must do, at a high level.

## Slide 19: Unified Datapath Design with Control
add, sub, and, or, slt, lw, sw

## Slide 20: Executing Branch Instructions
Read two operands from the register file
Use the ALU to compare the operands: subtract and check Zero signal
. . .
16-bit immediate
rt
rs
op
if GPR[rs] == GPR[rt] then
PC = PC + 4 + (imm << 2)

## Slide 21: Executing Branch Instructions
. . .
Calculate the branch target address:
- Sign-extend displacement (immediate from instruction)
- Shift left 2 places (MIPS uses word displacement – why?)
- Add to PC + 4 (already calculated PC + 4 during the instruction fetch)
Send computed branch target address to the PC (if taken)
16-bit immediate
rt
rs
op
if GPR[rs] == GPR[rt] then
PC = PC + 4 + (imm << 2)

## Slide 22: Aside: Branch Target Address
Examine the display below of a short MIPS assembly program, and the addresses at which the instructions will be loaded into memory when the program is executed:
address assembly source code
---------------------------------------------
.text
0x00400000 main: addi $s0, $zero, 10
0x00400004 addi $s1, $zero, 20
0x00400008 j check
0x0040000C repeat: sub $s3, $s1, $s0
0x00400010 sra $s3, $s3, 1
0x00400014 beq $s3, $zero, exit
0x00400018 add $s0, $s0, $s3
0x0040001C check: bne $s0, $s1, repeat
0x00400020 exit: li $v0, 10
0x00400024 syscall
If taken, a conditional branch causes the PC to be set to the address of the instruction that's the target of the branch:

## Slide 23: Aside: Branch Target Address
First of all, note that all the addresses are multiples of 4*.
Therefore, the "distance" between two instructions is always a multiple of 4.
*QTP: why isn't this surprising?
address assembly source code
---------------------------------------------
.text
0x00400000 main: addi $s0, $zero, 10
0x00400004 addi $s1, $zero, 20
0x00400008 j $check
0x0040000C repeat: sub $s3, $s1, $s0
0x00400010 sra $s3, $s3, 1
0x00400014 beq $s3, $zero, exit
0x00400018 add $s0, $s0, $s3
0x0040001C check: bne $s0, $s1, repeat
0x00400020 exit: li $v0, 10
0x00400024 syscall

## Slide 24: Aside: Branch Target Address
The immediate we store for a beq instruction is determined by the "distance" from the beq instruction to the instruction that is the target of the branch.
And note that this computation is done by the assembler when it creates the machine code representation of the instruction, not at runtime.
address assembly source code
---------------------------------------------
. . .
0x0040000C repeat: sub $s3, $s1, $s0
. . .
0x0040001C check: bne $s0, $s1, repeat
0x00400020 exit: li $v0, 10
. . .
However, while bne is being fetched:
- we have already computed PC + 4
- which is the address of the next instruction in memory
- so we need to compute the distance relative to the next instruction

## Slide 25: Aside: Branch Target Address
Here, that "distance" is 0x0C – 0x20 = – 0x14.
In 16-bit 2's complement, 0x14 represented as: 00000000 00010100
If the "distance" always ends in 00, there's no reason to store that 00 in the instruction…
address assembly source code
---------------------------------------------
. . .
0x0040000C repeat: sub $s3, $s1, $s0
. . .
0x0040001C check: bne $s0, $s1, repeat
0x00400020 exit: li $v0, 10
. . .

## Slide 26: Aside: Branch Target Address
Do we gain anything if we don't store those two 0's in the instruction?
Yes. We can store a 16-bit "distance" in the instruction, but effectively use an 18-bit "distance" at runtime.
That means that a conditional branch can "branch" farther… which is a gain.
address assembly source code
---------------------------------------------
. . .
0x0040000C repeat: sub $s3, $s1, $s0
. . .
0x0040001C check: bne $s0, $s1, repeat
0x00400020 exit: li $v0, 10
. . .
16-bit 2's complement range: -215 to 215-1
18-bit 2's complement range: -217 to 217-1

## Slide 27: Aside: Branch Target Address
address machine code
-------------------------------------------------------
. . .
0x0040000C
. . .
0x0040001C 000101 10000 10001 1111111111111011
0x00400020
. . .
Now, consider the machine code for our example:
The immediate in the beq instruction is: 1111111111111011
That's -5. If we shift that left by 2 bits (multiply by 4), we get -20 (0x14).
If we add -0x14 to the address 0x00400020, we get 0x0040000C, which is the target address we need.
target
bne
-0x14

## Slide 28: Executing Branch Instructions
beq
16-bit immediate
rt
rs
op
Adder computes branch target
ALU subtracts and sets Zero
rs and rt specify where operands are
AND gate controls which address goes to the PC
Control tells ALU to subtract operands,
sets Branch signal
Immediate is sign-extended and shifted

## Slide 29: Executing Jump Instructions
26-bit immediate
op
Calculate the jump target address:
- Shift left 2 places (just as with branch target address calculation)
- Concatenate with PC + 4[31:28] (already calculated PC + 4 during the instruction fetch)
Send computed jump target address to the PC
p31p30p29p28 i25i24i23i22…i3i2i1i0 00
from PC+4
PC = (PC+4)[31:28]|(IR[25:0] << 2)

## Slide 30: Aside: Jump Target Address
For jump (j) instructions, the 26-bit immediate is shifted 2 bits to the left, yielding a 28-bit offset, which is then added to the starting address of the current memory segment.
The calculation of the jump target address is similar to the calculation of the branch target address (beq).
*QTP: why?
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
1111111111111111111111111111 . . . 0000000000000000000000000000
0000
0001
1111
1110
. . .
0010
1101
The MIPS model is to view memory as a sequence of 256 MB segments.
The starting address of the current memory segment is given by the high 4 bits of PC + 4.*
Now, 256 MB can be addressed by 28-bit addresses.*
4GB address range

## Slide 31: Executing Jump Instructions
26-bit immediate
op
Control sets Jump signal so that the jump address will be used to fetch the next instruction
Calculate address of next sequential instruction
High 4 bits of PC + 4 specify "segment" containing this code.
MUX passes jump address back to PC
Concatenate to form 32-bit address for jump

## Slide 32: Unified Datapath
add, sub, and, or, slt, lw, sw, beq, j

## Slide 33: Summary
The unified datapath that we have designed:
- illustrates many of the logical issues that must be solved in designing any datapath
- can be extended to support additional instructions (easily for some, less so for others)
- is fundamentally unsatisfactory in that it requires a single clock cycle be long enough for every path within the datapath to stabilize before the next instruction is fetched
We may explore the second issue in exercises.
The third issue can only be dealt with by transforming the design to incorporate a pipeline.