## Slide 1: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
Non-stop speedup:
2n/(0.5n + 1.5) ≈ 4
Four loads:
- serial throughput:
0.5 load/hr
- pipelined throughput:
    1.14 load/hr
    - speedup:
    8/3.5 ≈ 2.3
Notes: QTP: for the pipelined version, calculate the throughput if we ran continuously until 2 am.
Soln: By 9:30 pm we have completed 4 jobs.
Thereafter, we complete another job every half hour.
There are 9 half-hour steps from 9:30 pm until 2 am.
So, by 2 am, we will have completed 13 jobs in 8 hours,
giving us a throughput value of 13/8 or 1.625.

## Slide 2: Basic Idea
What if we think of the simple datapath as a linear sequence of stages?
Can we operate the stages independently, using an earlier one to begin the next instruction before the previous instruction has completed?
We have 5 stages, which will mean that on any given cycle up to 5 different instructions will be in various points of execution.
Notes: 2

## Slide 3: MIPS 5-stage Pipeline
Stage Actions For
IF Instruction fetch from memory all
ID Instruction decode & register read decode for all;
read for all but j
EX Execute operation or calculate address all but j
MEM Access memory operand lw, sw
WB Write result back to register lw, R-type

## Slide 4: Timing Assumptions
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Instruction | Instruction fetch | Register read | ALU operation | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
j | ?? | ?? | ?? | ?? | ?? | ??
QTP: how does j fit in here?

## Slide 5: Pipeline Timing Details
Each stage is allotted 200ps, and so that is the cycle time.
That leads to "gaps" in stages 2 and 5:
We stipulate that register writes take place in the first half of a cycle and that register reads take place in the second half of a cycle.
QTP: why?

## Slide 6: Non-pipelined Performance
Single-cycle (Tc= 800ps)
Total time to execute 3 instructions would be 2400 ps.
Total time to execute N instructions would be 800N ps.

## Slide 7: Pipelined Performance
Pipelined (Tc= 200ps)
Total time to execute these 3 instructions would be 1400 ps.
Total time to execute N (similar) instructions would be 800 + 200N ps.
Speedup would be 2400/1400 or about 1.7.
Speedup would be 800N/(800+200N) or about 4 for large N.

## Slide 8: Pipeline Speedup
If all stages are balanced (i.e., all take the same time):
If not balanced, speedup is less
Speedup is due to increased throughput
  Latency (time for each instruction) does not decrease
  In fact…
Note: the goal here is to improve overall performance, which is often not the same as optimizing the performance of any particular operation.

## Slide 9: Pipelining and ISA Design
QTP: what if we had to support:
add 4($t0), 12($t1), -8($t2)
MIPS32 ISA was designed for pipelining:
32-bit machine instructions (uniformity)
- easier to fetch and decode in one cycle
- vs x86: machine instructions vary from 1 to 17 bytes
Few, regular instruction formats
- can decode opcode and read registers in same clock cycle
Load/store addressing
- can calculate address in one pipeline stage…
- … and access data memory in the next pipeline stage
Alignment requirements for memory operands
- 4-byte accesses must be at “word” addresses
- memory access takes only one clock cycle

## Slide 10: Issues
But… is there anything wrong with our thinking?
Notes: 10

## Slide 11: Issues
What about handling:
beq $s0, $s1, exit
j exit
lw $s0, 12($s1)
add $s3, $s0, $s1
add $s4, $s0, $s5
Are there any other issues…?