## Slide 1: Recap: the Basic Idea
Can we operate the stages independently, using an earlier one to begin the next instruction before the previous instruction has completed?
We have 5 stages, which will mean that on any given cycle up to 5 different instructions will be in various points of execution.
Notes: 1

## Slide 2: Hazards
Situations that prevent starting the next instruction in the next cycle
Structural hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 3: Structural Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store both require memory access
  So does instruction fetch
  Instruction fetch would have to stall for that cycle
Hence, MIPS pipeline require separate instruction/data memories
  Or separate instruction/data caches
  Or dual-ported memories
For example:

## Slide 4: Data Hazards
An instruction depends on completion of a write to a register by a previous instruction
add $s0, $t0, $t1 // writes $s0 from WB stage sub $t2, $s0, $t3 // needs value in ID stage
2-stage stall

## Slide 5: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath (& more control logic?)
no stall

## Slide 6: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed, can’t forward backward in time!
1-stage stall

## Slide 7: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles
Who reorders the code?

## Slide 8: Control Hazards: beq
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Register comparison done in EX stage
  MUX selection done in MEM stage
  Branch target address computed in EX stage
  What instruction do we fetch when BEQ is in ID stage?

## Slide 9: Control Hazards: beq
How can we deal with BEQ?
Stall until we know whether (& where) to branch?
Make the decision and calculate the address earlier?
Guess whether the branch will be taken?

## Slide 10: Stall on Branch
Wait until branch outcome determined before fetching next instruction
How many cycles does this cost?

## Slide 11: Early Decision
What new hardware would be needed to decide earlier?
Must compare the registers before the EX stage
Must compute the branch target address before the EX stage
Can we know what to do by the time BEQ enters the ID stage?

## Slide 12: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches will not be taken
  Fetch sequential instruction after branch, with no delay

## Slide 13: MIPS with Predict-Not-Taken
Prediction correct
Prediction incorrect

## Slide 14: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation