## Slide 1: Current Design

## Slide 2: Pipeline Timing Issues
Consider executing:
add $t2, $t1, $t0 # needs MemWrite = 0
sub $t3, $t1, $t0 # needs MemWrite = 0
or $t4, $t1, $t0 # needs MemWrite = 0
sw $t2, 0($t0) # needs MemWrite = 1
0
1
2
3
4
time
add
sub
or
sw
...

## Slide 3: Pipeline Timing Issues
What happens during cycle 4? Among other things…
- sw reaches the ID stage, and Control sets MemWrite to 1
- so, a memory write will occur while sub is in the MEM stage
- and that’s bad news…
0
1
2
3
4
time
add
sub
or
sw
...

## Slide 4: Pipeline Timing Issues
What needs to happen instead?
- the value of MemWrite that goes with sw…
- … needs to travel forward, stage to stage as sw does
0
1
2
3
4
time
add
sub
or
sw
...
0
1
2
3
4
time
sub
or
sw
...
...

## Slide 5: Pipeline Timing Issues
What needs to happen instead?
- the value of MemWrite that goes with sw…
- … needs to travel forward, stage to stage as sw does
So how do we make this happen?
0
1
2
3
4
time
or
sw
...
...
...

## Slide 6: Adding Buffers
Put storage buffers between adjacent stages:
Control writes/reads on these buffers with the clock signal.
Read values entering a stage from the “inbound” buffer.
Write values exiting a stage to the “outbound” buffer.
So no signal (or data value) arrives before its time…
outbound
inbound

## Slide 7: What now?
We have an idea: put buffers between adjacent stages and use those buffers to synchronize the operation of the pipeline stages
Are we sure we are handling all control signals properly… for every instruction?
Are there any values, other than control signals that must be passed through the interstage buffers?
Signals and values:
may move forward (from lower-numbered to higher-numbered stages)
can they ever move backward?
should they ever bypass the interstage buffers?
We will pick a particular instruction and consider its execution in detail…

## Slide 8: IF Stage for LW
PC+4 is computed,
stored back into the PC,
also stored in the IF/ID buffer although it will not be needed in a later stage for LW
Instruction word is fetched from memory,
and stored in the IF/ID buffer because it will be needed in the next stage.
Write into the buffer at end of clock cycle
Branch target address
Signal from AND

## Slide 9: ID Stage for LW
PC+4 is passed forward to ID/EX buffer...
Bits of load instruction are taken from IF/ID buffer, while
new instruction is being fetched back in stage 1.
16-bit field is fetched from IF/ID buffer, then sign-extended, then stored in the ID/EX buffer for use in a later stage.
Read register #1 and #2 contents are fetched and stored in ID/EX buffer until needed in next stage… #2 won't be needed.
Read from the buffer at beginning of cycle
Control signals passed forward.
Some to be used in later stages.
Some to be passed back here.
Old design:
Set write register in ID stage, but use from WB stage.
That doesn't work now…

## Slide 10: EX Stage for LW
PC+4 is taken from ID/EX buffer and added to branch offset…
Read register #1 contents are taken from ID/EX buffer and provided to ALU.
Read register #2 is passed forward to EX/MEM buffer, for possible use in later stage… but won't be needed.
Computed branch target address is stored in EX/MEM buffer to await decision in next stage... but won't be needed.
ALU result is stored in EX/MEM buffer for use as memory address in next stage.
Extended 16-bit literal is provided to ALU as second operand
Zero signal is stored in the EX/MEM buffer, but won't be needed.
Write register #

## Slide 11: MEM Stage for LW
Zero line taken from EX/MEM buffer for branch control logic in this stage…
ALU result is taken from EX/MEM buffer and passed to Address port of data memory.
Read register #2 contents taken from EX/MEM buffer and passed to Write data port of data memory.
ALU result also stored in MEM/WB buffer for possible use in last stage…
Value on Read data port of data memory is stored in MEM/WB buffer, awaiting decision in last stage..
Branch target address and signal from AND going back to MUX in IF stage
MemRead
Write register #

## Slide 12: WB Stage for LW
For load instructions, value from data memory is selected and passed back to register file.
The RegWrite signal is the one that goes with the load instruction (because it was sent forward through the interstage buffers).
MemtoReg
Write register port is now seeing the register number for the load instruction.
RegWrite
Write register #
Data to load

## Slide 13: Current Design
Here’s our revised configuration including the buffers:

## Slide 14: What now?
Would considering the execution of a different instruction yield new insights?
We will consider a similar instruction next: SW
Now, the IF stage is the same for all instructions, so we'll ignore it.

## Slide 15: EX Stage for SW
Almost the same as for LW…
Read register #2 is passed forward to EX/MEM buffer, for use in later stage… for SW this will be needed.
MemWrite

## Slide 16: MEM Stage for SW
Read register #2 contents taken from EX/MEM buffer and passed to Write data port of data memory.
Almost the same as for LW…
MemWrite
ALU result taken from EX/MEM buffer and passed to Address port of data memory.

## Slide 17: WB Stage for SW
For SW instructions, no value will be written to the register file… doesn't really matter which value we send back…
Not relevant for SW …

## Slide 18: Questions to Ponder
Can you repeat this analysis for other sorts of instructions, identifying in each stage what's relevant and what's not?
How much storage space does each interstage buffer need? Why?
Could adding interstage buffers affect the clock cycle? Why?

## Slide 19: Summary
Here’s our preliminary configuration for the buffers: