## Slide 1: Branch Hazards
Consider executing this sequence of instructions in the pipeline:
  address instruction
  ---------------------------------
  36: sub $10, $4, $8 40: beq $1, $3, L1 44: and $12, $2, $5 48: or $13,$12,$13
  52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: L1: lw $4, 50($7)
When beq moves into the ID stage:
- should we fetch the instruction at address 44?
- it may or may not be executed next, depending on whether $1 == $3
- we don’t know the address of the branch target instruction yet anyway

## Slide 2: Branch Hazards
  address instruction
  ---------------------------------
  36: sub $10, $4, $8 40: beq $1, $3, L1 44: and $12, $2, $5
  ... 72: L1: lw $4, 50($7)
When beq enters the ID stage, we don’t even know it is a conditional branch.
And… we won’t know if the branch should be taken until beq reaches the end of EX.
??? beq sub
Hey!
It’s a branch!

## Slide 3: Branch Hazards
So… we will have already fetched the next (sequential) instruction.
and beq sub
Hey!
It’s a branch!
  address instruction
  ---------------------------------
  36: sub $10, $4, $8 40: beq $1, $3, L1 44: and $12, $2, $5
  ... 72: L1: lw $4, 50($7)

## Slide 4: Stalling for Branch Hazards
Idea: insert stalls until we know if the branch will be taken.
We can’t act on that information before beq reaches the MEM stage.
Note:
the AND gate fires quickly enough that we can still fetch the branch target, on the same cycle, if the branch is taken.

## Slide 5: Stalling Until Branch Decision
  cycle action beq
  ----------------------------
  0: fetch sub 1: fetch beq IF 2: fetch and ID 3: stall EX
  4: stall MEM 5: fetch and/lw
Idea: insert stalls until we know if the branch will be taken.
That’s expensive.
If we don’t take the branch, we needlessly delayed the and instruction for 2 cycles.
fetch stall stall beq sub
Hamlet
Hamlet
Branch!
or
Don’t branch!

## Slide 6: Rollback for Branch Hazards
Idea: proceed as if the branch will not be taken;
turn mis-fetched instructions into nops if wrong.
If branch is taken, flush* these instructions
(set control values to 0)
*QTP: will this be too late?

## Slide 7: Questions
Questions to ponder:
- What about calculating the branch target address?
Can that be done in the ID stage?
- What about the register comparison?
Can that be done in the ID stage?
What about other kinds of conditional branches (e.g., bgez,)?
Could we rearrange the datapath so that the branch decision could be made earlier?

## Slide 8: Making Branch Decisions Earlier
Stall if branch is taken, proceed normally otherwise:
and beq
or and beq
lw nop beq
Cost is now one stall if branch is taken, nothing if branch is not taken.

## Slide 9: Making Branch Decisions Earlier
We can determine if the branch will be taken before beq reaches the EX stage.
Ideas: simple hardware suffices to compare two registers
moving the branch adder is relatively simple
But we also need to create a stall for one cycle…

## Slide 10: Stall-on-Branch
Whenever we decode a beq instruction:
QTP
Does this design actually accomplish that?
- we need to stall the instruction that follows the beq
- we have the ability to turn the instruction in the ID stage into a nop
- but we need to trigger that one cycle after decoding the beq

## Slide 11: The Big (but not quite final) Picture

## Slide 12: Data Hazards for Branches
If a comparison register in beq is a destination of 2nd or 3rd preceding R-type instruction
Can resolve using forwarding, without any stalls
add $3, $1, $4
sub $4, $5, $6
add $1, $2, $3
beq $1, $4, target
beq
add
sub

## Slide 13: Data Hazards for Branches
If a comparison register is a destination of the immediately-preceding type instruction or 2nd preceding load instruction
  Need to stall beq for 1 cycle
beq stalled
add $4, $5, $6
lw $1, addr
beq $1, $4, target
beq
lw
add
nop
nop
nop

## Slide 14: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need to stall for 2 cycles
beq stalled
beq stalled
lw $1, addr
beq $1, $0, target
beq
lw
nop
nop
nop
nop
nop
nop

## Slide 15: Data Hazards for Branches
So, the latest version of the datapath will require more modifications:
- these hazards must be detected in by new hardware in the ID stage
- the actual forwarding (substitution) operations also require new hardware in the ID stage
These changes are similar to the earlier discussion of forwarding.
Details are left as an exercise.
- handling these hazards requires stalling, as with lw, but…
- if the writing instruction is one cycle ahead of beq we need 2 stall cycles
- if the writing instruction is two cycles ahead of beq we need 1 stall cycle