## Slide 1: Cache Memory and Performance
Many of the following slides are taken with permission from
Complete Powerpoint Lecture Notes for Computer Systems: A Programmer's Perspective (CS:APP)
Randal E. Bryant and David R. O'Hallaron
http://csapp.cs.cmu.edu/public/lectures.html
The book is used explicitly in CS 2505 and CS 3214 and as a reference in CS 2506.

## Slide 2: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
CPU looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 3: General Cache Organization (S, K, B)
K = 2k lines (blocks) per set
S = 2s sets
set
Cache size:
C = S x K x B data bytes
B = 2b bytes per cache block (the data)
0
1
2
3
2s-1
0
1
2k-1
line (block)
0
1
2
B-1
tag
v
valid bit

## Slide 4: Cache Defines View of DRAM
The "geometry" of the cache is defined by:
S = 2s the number of sets in the cache
K = 2k the number of lines (blocks) in a set
B = 2b the number of bytes in a line (block)
These values define a related way to think about the organization of DRAM:
DRAM consists of a sequence of blocks of B bytes.
The bytes in a block (line) can be indexed by using b bits.
DRAM consists of a sequence of groups of S blocks (lines).
The blocks (lines) in a group can be indexed by using s bits.
Each group contains SxB bytes, which can be indexed by using s + b bits.

## Slide 5: Cache (8, 2, 4) and 256-Byte DRAM
K = 21 blocks (lines) per set
S = 23 sets
Cache size:
C = S x K x B = 64 data bytes
0
0
1
0
1
5
6
7
4
3
2
0
1
2
tag
v
B = 22 bytes per cache block (the data)
valid bit
3
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
. . . | . .
252 | 
253 | 
254 | 
255 | 
DRAM

## Slide 6: Cache View of DRAM
So, to generalize, suppose a cache has:
S = 2s sets
K = 2k blocks (lines) per set
B = 2b bytes per block (line)
And, suppose that DRAM uses N-bit addresses. then for any address:
aN-1 … as+b as+b-1 … ab ab-1 … a0
Bits ab-1:a0 give the byte index within the block
Bits ab+s-1:ab give the set index
Bits aN-1:as+b become the tag for the data
Note that these bits are only the same for blocks that are within the same DRAM group.

## Slide 7: Cache Read
t bits
s bits = K
b bits = J
Address of word:
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset
Line
Set
0
1
K
2s-1
0
1
2k-1
K
0
1
2b-1
tag
v
J
set
index
1
tag
2
3
block
offset
data begins at this offset
4

## Slide 8: Example: Direct Mapped Cache (K = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 9: Example: Direct Mapped Cache (K = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
block offset
tag
matching tags  hit
valid? +

## Slide 10: Example: Direct Mapped Cache (K = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
int (4 Bytes) is here
block offset
No match: old line (block) is evicted and replaced by requested block from DRAM
matching tags  hit
valid? +

## Slide 11: K-way Set Associative Cache (Here: K = 2)
K = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 12: K-way Set Associative Cache (Here: K = 2)
K = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
block offset
tag
matching tags  hit
valid? +

## Slide 13: K-way Set Associative Cache (Here: K = 2)
K = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
matching tags  hit
valid? +

## Slide 14: Cache Organization Types
The "geometry" of the cache is defined by:
S = 2s the number of sets in the cache
K = 2k the number of lines (blocks) in a set
B = 2b the number of bytes in a line (block)
K = 1 (k = 0) direct-mapped cache
only one possible location in cache for each DRAM block
S > 1
K > 1 K-way associative cache
K possible locations (in same cache set) for each DRAM block
S = 1 (only one set) fully-associative cache
K = # of cache blocks each DRAM block can be at any location in the cache

## Slide 15: Cache Example
5-bit addresses (32-word DRAM)
Direct-mapped, 8-blocks, 1 word/block
Index | Valid | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 0 |  | 
111 | 0 |  | 

## Slide 16: Cache Example
Index | Valid | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 0 |  | 
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Memory access
address 10 110
hit? N
10 110
address % #sets
set to hold data
address / #sets
set to hold data

## Slide 17: Cache Example
Index | Valid | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Memory access
address 11 010
hit? N
11 010
address % #sets
set to hold data
address / #sets
set to hold data

## Slide 18: Cache Example
Index | Valid | Tag | Data
000 | 0 |  | 
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 |  | 
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Memory access
address 10 110
Identify the cache slot
If valid bit is 1…
and tags match... hit!

## Slide 19: Cache Example
Index | Valid | Tag | Data
000 | 0 | 10 | Mem[10000]
001 | 0 |  | 
010 | 1 | 11 | Mem[11010]
011 | 0 | 00 | Mem[00011]
100 | 0 |  | 
101 | 0 |  | 
110 | 1 | 10 | Mem[10110]
111 | 0 |  | 
Memory accesses
address 10 000 miss
address 00 011 miss
address 10 000 hit

## Slide 20: Cache Example
Index | Valid | Tag | Data
. . . |  |  | 
010 | 1 | 11 | Mem[11010]
. . . |  |  | 
Memory access
address 10 010 miss (tags don't match)
Index | Valid | Tag | Data
. . . |  |  | 
010 | 1 | 10 | Mem[10010]
. . . |  |  | 
replacement

## Slide 21: Block Size Considerations
Larger blocks should reduce miss rate
  - due to spatial locality (if present)
But in a fixed-sized cache
  - larger blocks  fewer of them
    more competition  increased miss rate
  - larger blocks  pollution
Larger miss penalty
  - can override benefit of reduced miss rate
  - early restart and critical-word-first can help

## Slide 22: Cache Misses
On cache hit, CPU proceeds normally
On cache miss:
  - stall the CPU pipeline
  - fetch block from next level of hierarchy
  - instruction cache miss
    restart instruction fetch
  - data cache miss
    complete data access

## Slide 23: Write-Through
On data-write hit, could just update the block in cache
  - but then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  - e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    - effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  - holds data waiting to be written to memory
  CPU continues immediately
    - only stalls on write if write buffer is already full

## Slide 24: Write-Back
Alternative: On data-write hit, just update the block in cache
  - keep track of whether each block is dirty
When a dirty block is replaced
  - write it back to memory
  - can use a write buffer to allow replacing block to be read first

## Slide 25: Write-Allocation
What should happen on a write miss?
Alternatives for write-through
  - allocate on miss: fetch the block
  - write around: don’t fetch the block
    since programs often write a whole block before reading it
    (e.g., initialization)
For write-back
  - usually fetch the block

## Slide 26: DRAM Supporting Caches
Use DRAMs for main memory
  - fixed width (e.g., 1 word)
  - connected by fixed-width clocked bus
    - bus clock is typically slower than CPU clock
Example cache block read
  - 1 bus cycle for address transfer
  - 15 bus cycles per DRAM access
  - 1 bus cycle per data transfer
For 4-word block, 1-word-wide DRAM
  - miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  - bandwidth = 16 bytes / 65 cycles = 0.25 B/cycle

## Slide 27: Measuring Cache Performance
Components of CPU time
  - program execution cycles
    - includes cache hit time
  - memory stall cycles
    - mainly from cache misses
With simplifying assumptions:

## Slide 28: Cache Performance Operation
Given
  - I-cache miss rate = 2%
  - D-cache miss rate = 4%
  - miss penalty = 100 cycles
  - base CPI (ideal cache) = 2
Miss cycles per instruction
  - I-cache: 0.02 × 100 = 2
  - D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  - ideal CPU is 5.44/2 =2.72 times faster

## Slide 29: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  - CPU with 1ns clock,
  hit time = 1 cycle,
  miss penalty = 20 cycles,
  I-cache miss rate = 5%
  - AMAT = 1 + 0.05 × 20 = 2ns (2 cycles per instruction)

## Slide 30: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 31: Associative Caches
Fully associative
  - allow a given block to go in any cache entry
  - requires all entries to be searched at once
  - comparator per entry (expensive)
K-way set associative
  - cach set contains K entries
  - block number determines which set
    (Block number) modulo (#Sets in cache)
  - search all entries in a given set at once
  - K comparators (less expensive)

## Slide 32: Associative Cache Example

## Slide 33: Spectrum of Associativity
Capacity: 8 blocks of user data

## Slide 34: Associativity Example
Compare 4-block caches
  - direct mapped vs 2-way set associative vs fully associative
  - block access sequence: 0, 8, 0, 6, 8
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
Direct mapped

## Slide 35: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
Fully associative

## Slide 36: How Much Associativity?
Increased associativity decreases miss rate
  - but with diminishing returns
Simulation of a system with 64KB
D-cache, 16-word blocks, SPEC2000
  - 1-way: 10.3%
  - 2-way: 8.6%
  - 4-way: 8.3%
  - 8-way: 8.1%

## Slide 37: Set Associative Cache Organization
Compare the tag we’re trying to match to all of the tags for blocks in the relevant set at the same time!
Then factor in the valid bits, also in parallel.
And employ a MUX

## Slide 38: Replacement Policy
Direct mapped: only one choice
Set associative
  - prefer non-valid entry, if there is one
  - otherwise, choose among entries in the set
Least-recently used (LRU)
  - choose the one unused for the longest time
    simple for 2-way, manageable for 4-way, too hard beyond that
Random
  - gives approximately the same performance as LRU for high associativity

## Slide 39: Multilevel Caches
Primary (L-1) cache attached to CPU
  - small, but fast
Level-2 cache services misses from primary cache
  - larger, slower, but still faster than main memory
Some high-end systems include L-3 cache
Main memory services L-2 cache misses

## Slide 40: Multilevel Cache Example
Given
  - CPU base CPI = 1, clock rate = 4GHz
  - miss rate/instruction = 2%
  - main memory access time = 100ns
With just primary cache
  - miss penalty = 100ns / 0.25ns = 400 cycles
  - effective CPI = 1 + 0.02 × 400 = 9

## Slide 41: Multilevel Cache Example
Now add L-2 cache
  - access time = 5ns
  - global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  - penalty = 5ns / 0.25ns = 20 cycles
Primary miss with L-2 miss
  - extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 42: Multilevel Cache Considerations
Primary cache
  - focus on minimal hit time
L-2 cache
  - focus on low miss rate to avoid main memory access
  - hit time has less overall impact
Results
  - L-1 cache usually smaller than a single monolithic cache
  - L-1 block size smaller than L-2 block size (then again…)

## Slide 43: Example: Intel Core i7 Cache
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
2700 Series
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 25-40 cycles
Block size: 64 bytes for all caches.