## Slide 1: Transactional Memory
Part 1: Concepts and Hardware- Based Approaches

## Slide 2: Introduction
Provide support for concurrent activity using transaction-style semantics without explicit locking
Avoids problems with explicit locking
  Software engineering problems
  Priority inversion
  Convoying
  Deadlock
Approaches
  Hardware (faster, size-limitations, platform dependent)
  Software (slower, unlimited size, platform independent)
    Word-based (fine-grain, complex data structures)
    Object-based ( course-grain, higher-level structures)

## Slide 3: History
D.B. Lomet, “Process structuring, synchronization, and recovery using atomic actions,”
In Proc. ACM Conf. on Language Design for Reliable Software, Raleigh, NC, 1977,
pp. 128–137.
Lomet* proposed the construct:
<identifier>: action( <parameter-list> );
<statement-list>
end;
where the statement-list is executed as an atomic action. The statement-list can include:
await <test> then <statement-list>;
so that execution of the process/thread does not proceed until test is true.
*

## Slide 4: Transaction Pattern
repeat {
BeginTransaction(); /* initialize transaction */
<read input values>
success = Validate(); /* test if inputs consistent */
if (success) {
<generate updates>
success = Commit(); /* attempt permanent update */
if (!success)
Abort(); /* terminate if unable to commit */
}
EndTransaction(); /* close transaction */
} until (success);

## Slide 5: Guarantees
Wait-freedom
  All processes make progress in a finite number of their individual steps
  Avoid deadlocks and starvation
  Strongest guarantee but difficult to provide in practice
Lock-freedom
  At least one process makes progress in a finite number of steps
  Avoids deadlock but not starvation
Obstruction-freedom
  At least one process makes progress in a finite number of its own steps in the absence of contention
  Avoids deadlock but not livelock
  Livelock controlled by:
    Exponential back-off
    Contention management

## Slide 6: Hardware Instructions
Compare-and-Swap (CAS):
Usage: a spin-lock
inuse = false;
…
while (CAS(&inuse, false, true);
Examples:
CMPXCHNG instruction on the x86 and Itaninium architectures
word CAS (word* addr, word test, word new) {
atomic {
if (*addr == test) {
*addr = new;
return test;
}
else return *addr;
}
}

## Slide 7: Hardware Instructions
ldl_l/stl_c and ldq_l/stq_c (Alpha), lwarx/stwcx (PowerPC), ll/sc (MIPS), and ldrex/strex (ARM version 6 and above).
LL/SC: load-linked/store-conditional
Examples:
word LL(word* address) {
return *address;
}
boolean SC(word* address, word value){
atomic { if (address updated since LL)
return false;
else { address = value;
return true;
}
}
}
Usage:
repeat { while (LL(inuse));
done = SC(inuse, 1);
} until (done);

## Slide 8: Hardware-based Approach
Replace short critical sections
Instructions
  Memory
    Load-transactional (LT)
    Load-transactional-exclusive (LTX)
    Store-transactional (ST)
  Transaction state
    Commit
    Abort
    Validate
Usage pattern
  Use LT or LTX to read from a set of locations
  Use Validate to ensure consistency of read values
  Use ST to update memory locations
  Use Commit to make changes permanent
Definitions
  Read set: locations read by LT
  Write set: locations accessed by LTX or ST
  Data set: union of Read set and Write set

## Slide 9: Example
typedef struct list_elem { struct list_elem *next; /* next to dequeue */
struct list_elem *prev; /* previously enqueued */
int value; } entry;
shared entry *Head, *Tail;
void list_enq(entry* new) {
entry *old_tail;
unsigned backoff = BACKOFF_MIN;
unsigned wait;
new->next = new->prev = NULL;
while (TRUE) {
old_tail = (entry*) LTX(&Tail);
if (VALIDATE()) {
ST(&new->prev, old_tail);
if (old_tail == NULL) {ST(&Head, new); }
else {ST(&old_tail->next, new); }
ST(&Tail, new);
if (COMMIT()) return;
}
wait = random() % (01 << backoff); /* exponential backoff */
while (wait--);
if (backoff < BACKOFF_MAX) backoff++;
}
}

## Slide 10: Hardware-based Approach

## Slide 11: Cache Implementation
Processor caches and shared memory connected via shared bus.
Caches and shared memory “snoop” on the bus and react (by updating their contents) based on observed bus traffic.
Each cache contains an (address, value) pair and a state; transactional memory adds a tag.
Cache coherence: the (address, value) pairs must be consistent across the set of caches.
Basic idea: “any protocol capable of detecting accessibility conflicts can also detect transaction conflict at no extra cost.”
Shared Memory
Bus
address
value
state
tag
cache
. . .

## Slide 12: Line States
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Access | Shared? | Modified?
invalid | none | --- | ---
valid | R | yes | no
dirty | R, W | no | yes
reserved | R, W | no | no

## Slide 13: Transactional Tags
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Meaning
EMPTY | contains no data
NORMAL | contains committed data
XCOMMIT | discard on commit
XABORT | discard on abort

## Slide 14: Bus cycles
Shared Memory
Bus
address
value
state
tags
cache
. . .
Name | Kind | Meaning | New access
READ | regular | read value | shared
RFO | regular | read value | exclusive
WRITE | both | write back | exclusive
T_READ | transaction | read value | shared
T_WRITE | transaction | read value | exclusive
BUSY | transaction | refuse access | unchanged

## Slide 15: Scenarios
LT instruction
  If XABORT entry in transactional cache: return value
  If NORMAL entry
    Change NORMAL to XABORT
    Allocate second entry with XCOMMIT (same data)
    Return value
  Otherwise
    Issue T_READ bus cycle
      Successful: set up XABORT/XCOMMIT entries
      BUSY: abort transaction
LTX instruction
  Same as LT instruction except that T_RFO bus cycle is used instead and cache line state is RESERVED
ST instruction
  Same as LTX except that the XABORT value is updated

## Slide 16: Performance Simulations
comparison methods
  TTS – test/test-and-set (to implement a spin lock)
  LL/SC – load-linked/store-conditional (to implement a spin lock)
  MCS – software queueing
  QOSB – hardware queueing
  Transactional Memory
QOSB
TTS
MCS
LL/SC
TM