## Slide 1: CS 4284 Systems Capstone
Project 4 Hints

## Slide 2: Project 4
Final Task: Build a simple file system!
  “Easier than Project 3” – maybe
  But: definitely more lines of code for complete solution
    And no room for errors – it’s a filesystem, after all!
Subtasks:
  Buffer Cache
  Extensible Files
  Subdirectories
Again open-ended design problem
Synchronization

## Slide 3: How Pintos’s Filesystem Is Used
bootloader
kernel
filesystem block dev
scratch block dev
swap block dev
extract
append
pintos script
writes/reads
files
your kernel
is loaded from
VM swapping
pintos applications

## Slide 4: Project Requirements
Your kernel must
  Be able to format the file system block device when asked (write structures for an initial, empty filesystem on it)
  Be able to copy files onto it when called from fsutil_extract() (which happens before process_execute is called for the first time) – and copy files off of it
  Be able to support required system calls
    New calls: mkdir, readdir, inumber, isdir, chdir
  Be able to write data back to persistent storage
  Be able to copy files from it when called from fsutil_append()

## Slide 5: Project Requirements (cont’d)
Only your kernel writes to and reads from your disk
Don’t have to follow any prescribed layout
Can pick any layout strategy that doesn’t suffer from external fragmentation and can grow files
  If you lack better ideas, use Unix-style direct, single indirect, double indirect inode layout
Can pick any on-disk inode layout (you must design your own, the existing one does not work)
Can pick any directory layout (although existing directory layout suffices)

## Slide 6: Base Filesystem Layout
Disk Sectors
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |  | . | . | . | . | . | . | . | . | .
Root Directory (16 entries à 20bytes < 1 sector) |  |  | 
inode # name[15] inuse=0 | inode # name[15] inuse=0 | inode # name[15] inuse=0 | inode # name[15] inuse=0
Root Directory Inode Start=6 Length=1
multi-oom executable
File Inode Start=8 Length=5
inode #7 multi-oom inuse=1
Freemap File Inode Start=2 Length=4
Free Map 11100101

## Slide 7: Recommended Order
Buffer Cache – implement & pass all regression tests
Extensible Files – implement & pass file growth tests
Subdirectories
Miscellaneous: cache readahead, reader/writer fairness, deletion etc.
Synchronization
(at some point) drop global fslock
You should think about synchronization throughout

## Slide 8: The Big Picture
PCB
…
5
4
3
2
1
0
Data structures to keep track of open files
struct file
inode + position
struct dir
inode + position
struct inode
Per-process file descriptor table
Buffer Cache
Open file table
Free Map
files (including directories) inodes, index blocks
Cached data and metadata in buffer cache
On-Disk Data Structures
?
Root Dir Inode

## Slide 9: Buffer Cache (1): Overview
Should cache accessed disk blocks in memory
Buffer cache should be only interface to disk: all disk accesses should go through it
  Ensures consistency!
file_*()
dir_*()
inode_*()
cache_*()
block_*()
system calls, fs utils

## Slide 10: Buffer Cache (2): Design
512 bytes
512 bytes
512 bytes
512 bytes
512 bytes
512 bytes
512 bytes
64
desc
desc
desc
desc
desc
desc
desc
Cache Block Descriptor
disk_sector_id, if in use
dirty bit
valid bit
# of readers
# of writers
# of pending read/write requests
lock to protect above variables
signaling variables to signal availability changes
usage information for eviction policy
data (pointer or embedded)

## Slide 11: Buffer Cache (3): Interface
// cache.h
struct cache_block; // opaque type
// reserve a block in buffer cache dedicated to hold this sector
// possibly evicting some other unused buffer
// either grant exclusive or shared access
struct cache_block * cache_get_block (disk_sector_t sector, bool exclusive);
// release access to cache block
void cache_put_block(struct cache_block *b);
// read cache block from disk, returns pointer to data
void *cache_read_block(struct cache_block *b);
// fill cache block with zeros, returns pointer to data
void *cache_zero_block(struct cache_block *b);
// mark cache block dirty (must be written back)
void cache_mark_block_dirty(struct cache_block *b);
// not shown: initialization, readahead, shutdown

## Slide 12: Buffer Cache (4): Notes
Interface is just a suggestion
Definition as static array of 64 blocks ok
Use structure hiding (don’t export cache_block struct outside cache.c)
Must have explicit per-block locking (can’t use Pintos’s lock since they do not allow for multiple readers)
Should provide solution to multiple reader, single writer synchronization problem that starves neither readers nor writers:
  Use condition variables!
Eviction: use LRU (or better)
  Can use Pintos list_elem to implement eviction policy, such as LRU via stack implementation

## Slide 13: Buffer Cache (5): Prefetching
Would like to bring next block to be accessed into cache before it’s accessed
Must be done in parallel
  use daemon thread and producer/consumer pattern
Note: next(n) not always equal to n+1
Don’t initiate read_ahead if next(n) is unknown or would require another disk access to find out
b = cache_get_block(n, _);
cache_read_block(b);
cache_readahead(next(n));
queue q;
cache_readahead(sector s) {
q.lock();
q.add(request(s));
qcond.signal();
q.unlock();
}
cache_readahead_daemon() {
while (true) { q.lock();
while (q.empty())
qcond.wait();
s = q.pop();
q.unlock();
read sector(s);
}
}

## Slide 14: Multi-Level Indices
Need only single&double indirect blocks
1
2
3
.. N
FLI
SLI TLI
1
2
index
N
index2
index
index
N+I
N+1
N+I+1
index3
index2
Direct
Blocks
Indirect
Block
Double Indirect
Block
Triple Indirect
Block
index
N+I+I2

## Slide 15
34
35
0
1
2
3
4
5
6
7
12
13
14
20
21
27
28
Logical View (Per File)
offset in file
Physical View (On Disk) (ignoring other files)
Inode
Data
Index
Index2
sector numbers on disk

## Slide 16
34
35
0
1
2
3
4
5
6
7
12
13
14
20
21
27
28
Logical View (Per File)
offset in file
Physical View (On Disk) (ignoring other files)
Inode
Data
Index
Index2
sector numbers on disk
…
5
12
4
3
2
1
…
10
11
9
8
7
6
…
-1
-1
34
27
20
13
…
18
19
17
16
15
14

## Slide 17: Multi-Level Indices (cont’d)
How many levels do you need?
  Worst case: single, large file spans entire disk
Max Disk size: 8MB = 16,384 Sectors
Assume sector number takes 2 or 4 bytes, can store 256 or 128 in one sector
Filesize(using only direct blocks) < 256
Filesize(direct + single indirect block) < 2*256
File (direct + single indirect + double indirect) < 2*256 + 256^2 = 66,048

## Slide 18: Files vs. Inode vs. Directories
Offset management in struct file etc. should not need any changes
  If there’s no sharing of struct file/dir instances between processes, then there are no concurrency issues since Pintos’s processes are single-threaded!
You have to completely redesign struct inode_disk to fit your layout
You will have to change struct inode
  struct inode are necessarily shared between processes – since they represent files on disk!
  struct inode can no longer embed struct inode_disk (inode_disk should be stored in buffer cache)

## Slide 19: struct inode vs struct inode_disk
struct inode_disk
{
disk_sector_t start; /* First data sector. */
off_t length; /* File size in bytes. */
unsigned magic; /* Magic number. */
uint32_t unused[125];/* Not used. */
};
/* In-memory inode. */
struct inode
{
struct list_elem elem; /* Element in inode list. */
disk_sector_t sector; /* Sector number of disk location. */
int open_cnt; /* Number of openers. */
bool removed; /* True if deleted, false otherwise. */
int deny_write_cnt; /* 0: writes ok, >0: deny writes. */
struct inode_disk data; /* Inode content. */
};
store in buffer cache
redesign for indexed approach

## Slide 20: Extending a file
Seek past end of file & write extends a file
Space in between logically contains zeros
  Can extend sparsely (use “nothing here” marker in index blocks)
Consistency guarantee on file extension:
  If A extends & B reads, B may read all, some, or none of what A wrote
    But never something else!
  Implication: do not update & unlock metadata structures (e.g., inode length) until data is in buffer cache

## Slide 21: Subdirectories
Support nested directories (work as usual)
Requires:
  Keeping track of type of file in on-disk inode
  Distinction between file descriptors in syscall layer – e.g., must reject write() to open directory
Should only require minor changes to how individual directories are implemented (e.g., as a linear list – should be able to reuse existing code)
  Must implement “.” and “..” – simple solution is to create the two entries on disk when a directory is created.
  Must support path names such as ///a/b/../c/./d
  Path components can remain <= 14 in length
  Once file growth works, directory growth should work “automatically”
Implement system calls: readdir, mkdir, rmdir
  Need a way to test whether directory is empty
  readdir() should not return . and ..

## Slide 22: Subdirectories: Lookup
Implement absolute & relative paths
Use strtok_r to split path
  Recall that strtok_r() destroys its argument - make sure you create copy if necessary
  Make sure you operate on copied-in string
Walk hierarchy, starting from root directory (for absolute paths); current directory (for relative paths)
All components except last must exist & be directories
Make sure you don’t leak memory, or you fail dir-vine.

## Slide 23: Current Directory
Need to keep track of current directory
  in struct thread
  be aware of possible initialization order issues: before first task starts, extract/append must work but process_execute hasn’t been called; at that time, assume that current directory is /
When an attempt is made to delete the current directory, or any open directory, either
  Reject (like Windows does, easier way?)
  Allow, but don’t allow further use (like Unix does)

## Slide 24: Synchronization Issues (1)
Always consider: what lock (or other protection mechanism) protects which field:
  If lock L protects data D, then all accesses to D must be within lock_acquire(&L); …. Update D …; lock_release(&L);
Embed locks in objects or define them as static variables where appropriate (e.g., struct inode and inode list lock)
For buffer cache entries, must build new synchronization structure (Single Writer/Multiple Reader lock without starvation) on top of existing ones (locks + condition variables)
For directories, could use lock on underlying inode directly to guarantee exclusive access while performing directory scans/updates

## Slide 25: Synchronization Issues (2)
Should be fine-grained: independent operations should proceed in parallel, for example
  Don’t lock entire buffer cache when waiting for read/write access of individual buffer cache entry
  Example: don’t lock entire path resolution component when looking up file along /a/b/c/d
  Files should support multiple readers & writers
    Data writes do not require exclusive access to buffer cache block holding the data!
  Process removing a file in directory A should not wait for removing file in directory B
For full credit, must have dropped global fs lock
  Can’t see whether any of this works until you have done so

## Slide 26: Free Map Management
Can leave almost unchanged
Read from disk on startup, flush on shutdown
Instead of allocating n sectors at file creation time, now allocate 1 sector at a time, and only when file is growing
  Implement extents for extra performance + credit
But: you must still support creating files that have an initial size greater than 0; easy to do:
  If file_create(“…”, m) is called with m > 0, perform regular create with size 0, then invoke inode_write_at(offset=m-1, 1byte of data) to expand to appropriate length
Don’t forget to protect free_map() with lock

## Slide 27: Grading Hints
Persistence tests won’t fully pass until file growth + subdirectories are sufficiently implemented such that ‘tar’ works.
Core parts (majority of credit) of assignment are
  Buffer cache
  Extensible files
  Subdirectories
For this assignment, credit for regression tests will depend on how many parts (n = 0, 1, 2) of the assignment you’ve implemented
  Credit for regression tests = Reported TestScore * n/3
  Don’t get credit for resubmitting P2.
Tests will not detect
  If you keep global fslock or not
  If you have a buffer cache
  Will grade those aspects by inspection/reading your design document
Good Luck!